## Slide 1: EE 444 Introduction to Computer Networks
Spring 2018

## Slide 2: Administrative Details
Instructor: Ece Guran Schmidt
Office: EC-207
Email: eguran@metu.edu.tr
Web page: http://users.metu.edu.tr/eguran/
Schedule: Tuesday: 13:40-15:30@D-131, Thursday: 10:40-11:30@A-208
My main research area is computer networking 
You can check out my web page to see what I do in my research

## Slide 3: Administrative Details
Follow
  https://odtuclass.metu.edu.tr/
  for lecture slides and announcements
  Your e123456@metu.edu.tr email
Queuing Lecture will be on the white board. Also other notes can be on the white board.
Lectures will be posted on odtuclass
Homework assignments, additional material, study questions are also on odtuclass

## Slide 4: Administrative Details
Communication:
  Preferred communication mean: E-MAIL
  Send with subject including ee444 (no guarantee of reply otherwise)
  I will answer your questions any time if you come by my office provided that I am not busy at the moment

## Slide 5: Required
Prerequisite(s):
An introductory course on Probability Theory (EE230).
Background Requirement(s):
One of EE441, EE445 or EE447 is strongly recommended.

## Slide 6: Advice
This is COMPUTER Networking class. Its primary audience is Computer Option Students.
I do not advise taking this class if you did not take any computer classes last semester.
This is your last term. You cannot replace this class. Any bad result might affect your graduation, GPA, transcript etc.
You have less load this semester I intend to make use of it 

## Slide 7: Text Books
Andrew S. Tanenbaum, David J. Wetherall, Computer Networks,
Ed.5, Prentice-Hall, 2011.
Computer Networking: A Top Down Approach , 5th edition / 6th edition. Jim Kurose, Keith Ross Addison-Wesley, 2009/2014
Copyright notice: Lecture Note Slides are compiled from the teaching material of these books, previous lecture notes of EE444 and additional resources. Part of the slides are entirely created by Ece Schmidt.

## Slide 8: Course Objective (Why should you take this course?)
Basic computer networking technologies
Layered approach/ Modular design/ Interfaces
Concepts of network performance
Performances of some classical networking architectures

## Slide 9: Course Outline (Tentative)
Introduction to Computer Networking
Basic Queuing Theory
Application Layer
Transport Layer
Network Layer and Routing
Data Link Layer
Medium Access Control Sublayer
Further subjects (we will decide what to talk about based on the time left at the end of the semester)

## Slide 10: (Maybe) Different than other classes
Teaches all major computer components of computer networks in one semester for completeness
No physical layer concepts (channel capacity, sampling, modulation, frequency, interference, noise etc. exist in this course)
Many components and their relations to each other
Both theoretical and practical concepts
COMPREHENSIVE COURSE A LOT OF STUFF

## Slide 11: Grading
Mid-term exam: 30% (One midterm!)
Final Exam: 35%
Quizzes: 25%
Practical Work: 10%
Attendance: 5% bonus if you attend 100% of the lectures. Proportionally decreased bonus down to 80% attendance (80% will get 3%).

## Slide 12: Grading: Bütünleme
The right to take the final: You need to satisfy both of the following requirements :
  Attend at least 2 quizzes OR attend the MIDTERM exam (make-up if you had a valid health excuse on the MIDTERM day). The valid excuse for missing the midterm must be provided before the final.
  Submit at least one homework
Your grade will be NA otherwise.
http://oidb.metu.edu.tr/son-yariyilina-kayitli-olan-onlisans-ve-lisans-ogrencileri-icin-butunleme-sinavlari-yonergesi.

## Slide 13: Quizzes
Minimum 1 quiz per week in class after add drop. First quiz: February 27th
Content: Class discussions in the previous lecture (s)
Most quizzes will be announced before, some will be pop quiz.
Most quizzes will be at the beginning of the lecture.
Out of X quizzes during the semester, Y highest grades will be included in the final grade.
There is no make up or health excuse for quizzes and attendance.
Bring a piece of paper and pencil with you to all lectures.

## Slide 14: Homework assignments/ Practical Work
Possible Written homework assignments, Programming assignments, use of a simulator software, demos.
There will be separate questions in the final exam that evaluate your understanding of these assignments or a separate exam.

## Slide 15: A Friendly Reminder
Attend the lectures and do not lose contact with the class!!
Especially towards the end of the semester
  Design project, Spring festival, Nice weather…
Idea: Do not focus on any exam. Just come to class and pay attention…and have fun!!!

## Slide 16: Introduction to Computer Networking

## Slide 17: Why do we need computer networking?
We want to exchange information between/among remote locations (not at the same physical location).
Run applications with different needs

## Slide 18: Exchanging information
Web Browsing (no loss, limited delay)
E-mail (no loss, delay is ok)
Multimedia streaming (Internet radio)
(some loss is ok, limited delay)
Server
Chat (no loss, limited delay)
P2P file transfer (no loss)
IP phone, Skype (some loss is ok, limited delay)
Internet: Between different geographical locations

## Slide 19: Exchanging information
Factory floor networking
for manufacturing systems
Real-time, limited delay, no loss
In vehicle networking
for X-by-wire applications
Example Application: break by wire
Embedded environments: Between different system components (micro controllers, sensors)

## Slide 20: Exchanging information
Network on Chip (NoC): Between different intellectual property blocks on chip
bandwidth

## Slide 21: Exchanging information
Different applications with different requirements
Different distances:
  Internet, Embedded Systems, Network on Chip
Different physical media:
  Copper wire, optical fiber, wireless
Different technologies:
  Gigabit Ethernet, 3G/4G/5G Wireless, SONET-SDH
Different speeds
  Kbps, Mbps, Gbps

## Slide 22: Speed of data transfer
Technology | Speed | Physical Medium | Application
Regular telephone service (POTS) | Up to 56 Kbps | twisted pair | Home and small business access
3G Wireless | 21 Mbps downstream 5.8 Mbps upstream | RF in space (wireless) | Simultaneous access to different services (voice, video etc), Web surfing, instant messaging
4G (LTE Advanced) | Peak download 1Gbps Peak upload 500Mbps | RF in space (wireless) | Simultaneous access to different services (voice, video etc), Web surfing, instant messaging
Fast Ethernet | 100 Mbps | 100BASE-T (twisted pair); 100BASE-T (twisted pair); 100BASE-T (optical fiber) | Most popular business local area network (LAN) Workstations with 10 Mbps Ethernet cards can plug into a Fast Ethernet LAN
Gigabit Ethernet | 1 Gbps | Optical fiber (and "copper" up to 100 meters) | Workstations/networks with 10/100 Mbps Ethernet plug into Gigabit Ethernet switches
OC-48 | 2.488 Gbps | Optical fiber | Backbone
OC-192 | 10 Gbps | Optical fiber | Backbone

## Slide 23: Basic Philosophy
Applications do not need to know how the network operates
Server
The computer network should be transparent to the application

## Slide 24: What does a Computer Network look like
How does A and B exchange information?
A
B

## Slide 25: Why do we need a network to exchange information? (1)
If you have two computers on two desks in the same room how would you make them communicate?
Just use a cross cable: Point to point communication
How many cables do you need for three computers (all three want to talk to each other)?
How about 1000 computers?
N2 problem!

## Slide 26: The N 2 Problem
For N users to be fully connected directly
Requires N(N – 1)/2 connections
Requires too many cables, too complicated
Inefficient & costly since connections not always on

## Slide 27: Networking with switches/routers: Idea
Use special network devices (router/switch)
Connect users on demand
Only N connections
N2 problem is moved inside the router/switch
1
2
3
N – 1
N
Router/ switch

## Slide 28: Switching: Switches and routers
On demand N to N I/O connection:
  Switch fabric: Special interconnection hardware in the switch/router
  Switches packets from inputs to outputs
A
C
3
2
1
Router/ switch
B
Inside: Crossbar switch fabric

## Slide 29: Why do we need a network to exchange information? (2)
If you have two computers in two different cities, can you still use a cross cable?
Point to point communication NOT usually practical
  Large set of devices would need impractical number of connections
  Devices are too far apart
Solution is a computer network

## Slide 30: What’s the Internet?
millions of connected computing devices: hosts = end systems
  running network apps
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
protocols: rules of communication
routers: special network devices
  On demand connection
Notes: 30

## Slide 31: What are the hosts?
Desktop or portable computers, smart phones
Cars
https://www.cnet.com/roadshow/news/bmw-basically-wants-you-to-live-work-inside-your-connected-car/
BMW connected drive

## Slide 32: What are the hosts?
Any thing!
“Internet of things”

## Slide 33: What’s the Internet: Protocols
Communications between computers require very specific unambiguous rules
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt
e.g., TCP, IP, HTTP, Skype, Ethernet
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
Notes: 33

## Slide 34: A human protocol and a computer network protocol
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
Notes: 34

## Slide 35: A closer look at network structure
network edge:
  Low-speed
  applications and hosts
network core:
  High-speed
  interconnected routers
  network of networks
access networks, physical media:
  Connection between edge and core
  Edge routers
  wired, wireless communication links
Notes: 35

## Slide 36: Access Networks: Digital Subscriber Line (DSL)
telephone
network
DSL
modem
home PC
home
phone
Internet
DSLAM
Existing phone line: 0-4KHz phone; 4-50KHz upstream data; 50KHz-4MHz downstream data
splitter
central
office
  uses existing telephone infrastructure
  modulates frequencies from 4000 Hz to as high as 4 MHz.
  up to 3.3 Mbps upstream and up to 24 Mbps downstream
  dedicated physical line to telephone central office

## Slide 37: Access Networks: Ethernet
100 Mbps
100 Mbps
100 Mbps
1 Gbps
server
Ethernet
switch
institutional
router
to institution’s ISP
typically used in companies, universities, etc
  10 Mbs, 100Mbps, 1Gbps, 10Gbps Ethernet
  today, end systems typically connect into Ethernet switch

## Slide 38: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  802.11b/g (WiFi): 11 or 54 Mbps
cellular wireless access
  provided by telco operator
  3G/4G (LTE)/5G
base
station
mobile
hosts
router
Notes: 38

## Slide 39: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”
Notes: 39

## Slide 40: Network Core: Circuit Switching
Similar to phone call:
1) Dial: Connection set up
2) Ring: Signaling
3) Talk: Data Transfer
4) Hang up: Connection tear down
Notes: 40

## Slide 41: Network Core: Circuit Switching
end-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
Signaling and call setup before data transfer are required
Notes: 41

## Slide 42: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division
Notes: 42

## Slide 43: Circuit Switching: TDM
Low bit rate input
lines from different sources
Low bit rate output
lines to different users
High bit rate multiplexed data stream
Single high speed channel
Fixed duration time slots allocated to each connection
Muliplexer gives exactly the same amount of time to each device connected to it.
This time slice is allocated even if a device has nothing to transmit.
MUX
DEMUX
Notes: 43
Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 44: Circuit switching
What is good?
  The quality! No delay, reliable service
How is it used?
  Digital Phone
  Example: Is Bankasi can buy a “1 Mbit/s circuit” between its Istanbul and Ankara headquarters from Turk Telekom
  Two buildings always stay physically connected
What is bad?
  Expensive, inefficient (stays on even if not used)

## Slide 45: Network Core: Packet Switching
Header: control information
each end-end data stream divided into packets

## Slide 46: Network Core: Packet Switching
each packet uses full link bandwidth
user A, B share network resources
resources used as needed
A
B
Router output port L
queue of packets
waiting for output
link
statistical
multiplexing
R
store and forward: packets move one hop at a time
  node receives complete packet before forwarding
Notes: 46

## Slide 47: Network Core: Packet Switching
A and B are connected to the router R on two different input ports.
A and B send packets at the same time
Both packets’ destination: output port L
One packet is transmitted the other one is stored in the queue
A
B
Router output port L
queue of packets
waiting for output
link
statistical
multiplexing
R
resource contention:
aggregate resource demand can exceed the available amount
congestion: packets queue, wait for link use
Notes: 47

## Slide 48: Packet Switching: Statistical Multiplexing
sequence of A & B packets has no fixed timing pattern
  bandwidth shared on demand: statistical multiplexing.
A
B
C
100 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link
Notes: 48

## Slide 49: Packet switching versus circuit switching
Example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Packet switching allows more users to use the network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
Notes: 49

## Slide 50: Packet switching
What is good?
  Efficiency: Multiple user pairs can use the same link at the same time (one packet at a time)
How is it used?
  Internet: Packets from all applications use the same links all the time
What is bad?
  Quality, no dedicated service
  My email packet can go before your voice (skype) packet

## Slide 51: Network Performance Criteria
Bounded delay
Small delay variation (jitter)
Small packet-loss probability
Maximum Throughput~100%
Service differentiation among classes of traffic
Example: For high class traffic packet loss ratio<10-10

## Slide 52
WE MOVE TO SEVIM TAN NEXT WEEK
D231

## Slide 53: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link temporarily exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers
Notes: 53

## Slide 54: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
Notes: 54

## Slide 55: Four sources of packet delay
A
B
propagation
transmission
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
Notes: 55

## Slide 56: Queueing delay
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
Notes: 56

## Slide 57
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender measures time interval between transmission and reply.
3 probes
3 probes
3 probes
“Real” Internet delays and routes
Notes: 57

## Slide 58: “Real” Internet delays and routes
tracert www.ece.cmu.edu
Three ROUNDTRIP delay measurements
Tracing route to www.ece.cmu.edu [128.2.131.66]over a maximum of 30 hops:
1 4 ms 9 ms 4 ms eeatm.eee.metu.edu.tr [144.122.166.1]
2 1 ms 1 ms 1 ms rt1.metu.edu.tr [144.122.2.1]
3 40 ms 44 ms 29 ms 144.122.1.21
4 12 ms 3 ms 3 ms 193.140.85.137
5 10 ms 12 ms 11 ms 193.140.0.150
6 31 ms 32 ms 32 ms ulakbim.mx1.bud.hu.geant.net [62.40.125.129]
7 46 ms 46 ms 46 ms 62.40.98.47
8 136 ms 136 ms 140 ms internet2-gw.mx1.fra.de.geant.net [62.40.125.18]
9 142 ms 142 ms 142 ms internet2-re-wash.3rox.net [192.88.115.82]
10 146 ms 146 ms 146 ms pod-i-nh.cmu.3rox.net [147.73.16.121]
11 147 ms 148 ms 147 ms CORE0-POD-I-DCNS.GW.CMU.NET [128.2.0.193]
12 143 ms 143 ms 143 ms POD-A-CORE0.GW.CMU.NET [128.2.0.154]
13 144 ms 145 ms 144 ms ECE-RTR-POD-A-CYH.GW.CMU.NET [128.2.35.210]
14 146 ms 146 ms 147 ms WWW.ECE.CMU.EDU [128.2.131.66]
Trace complete.
Notes: 58

## Slide 59: Delay Variation
Packets have variable delay because of changing network conditions
Jitter: Delay variation

## Slide 60: Packet loss
queue (aka buffer) preceding link in the router has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
Notes: 60

## Slide 61: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
BOTTLENECK
link capacity
Rc bits/sec

## Slide 62: Network Organization
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Notes: 62

## Slide 63: Solution: Layered Protocol Architecture
Task broken into subtasks
Layers (similar to software/hardware modules):
  each layer implements a service via its own internal-layer actions
  relying on services provided by layer below
Each layer in a component communicates with the layer above and below (vertical)
Peer layers in all components communicate (horizontal)

## Slide 64: Example Problem
Philosopher 1 has a message for Philosopher 2: I like rabbits
Goal: They should communicate as if they are directly talking to each other as peers
Philosopher 1
Lives in Location A
Speaks English
Philosopher 2
Lives in Location B
Speaks French

## Slide 65: Layered Protocol Architecture
The philosopher-translator-secretary architecture.
The philosopher
needs the
service
of the translator
The translator
needs the
service
of the secretary
The secretary
needs the
service
of the fax
The philosopher
needs the
service
of the translator
The translator
needs the
service
of the secretary
The secretary
needs the
service
of the fax

## Slide 66: Layered Protocol Architecture
Philosophers
are peers
Translators
are peers
Secretaries
are peers
Actual data transmission via fax

## Slide 67: What is a network layer
A module that has software and hardware components
Responsible for a certain task
  communicates with its peer on the other side to fulfill its task
  Requires that some other tasks are correctly carried out to fulfill its own purpose Uses the services of lower layers
  Provides service to upper layers such that they can fulfill their tasks
Notes: 67

## Slide 68: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
Modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in a procedure doesn’t affect rest of system
Any disadvantage?
Notes: 68

## Slide 69: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical
Notes: 69

## Slide 70: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
application
presentation
session
transport
network
link
physical
Introduction 1-70
Notes: 70

## Slide 71: OSI vs Internet Protocol Stack
application
transport
internet
link
physical
application
presentation
session
transport
network
link
physical
OSI: Theoretical
Internet Protocol Stack: Practical

## Slide 72: Layered Architecture: Application Layer
Application Layer:
  Ece wants to browse a web page located in a server in the US
  It should look as if 2 processes communicate on the same machine
  Network should be invisible: Network cloud
process
Ankara
process
host or
server
controlled by
app developer
application
application
host or
server
Pittsburgh

## Slide 73: Layered Architecture: Application Layer
Application Layer:
  Defines message formats between the processes
  Determines the order and timing of the messages
process
Ankara
process
host or
server
controlled by
app developer
Pittsburgh
application
host or
server
application
application

## Slide 74: Layered Architecture: Application Layer
Application Layer needs:
  Correct and in order delivery of the messages
Solution:
  Application layer uses the services of the Transport Layer
process
Ankara
process
host or
server
Internet
controlled by
app developer
host or
server
Pittsburgh
application
transport
application
transport

## Slide 75: Layered Architecture: Transport Layer
Transport Layer :
provides logical communication between app processes running on different hosts
run in end systems (hosts)
  send side: breaks app messages into segments, sends to the other host
  rcv side: reassembles segments into messages, passes to app layer
process
Ankara
process
host or
server
Internet
controlled by
app developer
Pittsburgh
application
transport
application
transport
host or
server

## Slide 76: Layered Architecture: Transport Layer
Transport Layer needs :
Actual delivery of the messages to the other machine over the network cloud
If the messages are delivered “somehow” the transport layer can provide the service of orderly delivery to the application layer
Solution:
  Transport Layer uses the services of the Network Layer
process
Ankara
process
host or
server
Internet
controlled by
app developer
Pittsburgh
application
transport
network
application
transport
network
host or
server

## Slide 77: Layered Architecture: Network Layer
Provides the service of sending the segment from sending to receiving host
Network layer protocols in every host, router
Router examines header fields in all packets passing through it
network
network
network
network
network
network
network
l
network
application
transport
network
application
transport
network

## Slide 78: Layered Architecture: Network Layer
Network Layer needs:
  To send the packet reliably from one node to other node
  Such that it gets to the destination node
Solution:
  Network Layer uses the services of the Data Link Layer
network
data link
network
data link
network
data link
network
data link
l
network
data link
network
data link
network
data link
network
data link
application
transport
network
data link
application
transport
network
data link

## Slide 79: Layered Architecture: Data Link Layer
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
Data-link layer:
  has responsibility of
  transferring datagram from one node
  to adjacent node over a link

## Slide 80: Layered Architecture: Data Link Layer
Data Link Layer needs:
  To actually send the information to the next node
Solution:
  Data Link Layer uses the services of the Physical Layer
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 81: Layered Architecture: Physical Layer
Provides the means to transmit bits from sender to receiver
Data must be transformed to electromagnetic signals to be transmitted.
Representing information in signals
  How much can be represented
  How to represent, how to interpret
Transmission media

## Slide 82: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
Notes: 82

## Slide 83: Current Internet
https://www.caida.org/research/topology/as_core_network/2017/

## Slide 84: Current Internet
https://www.cisco.com/c/en/us/solutions/collateral/service-provider/visual-networking-index-vni/vni-hyperconnectivity-wp.html

## Slide 85: Hosts

## Slide 86: Applications

## Slide 87
MIDTERM: 11th of APRIL WEDNESDAY 840
FIRST QUIZ 27th of FEBRUARY 1340 in Class
DON’T BE LATE

## Slide 88: Introduction to Computer Networking