## Slide 1: Data Link Layer Part VI: IEEE 802.11 wireless LANs (“Wi-Fi”)

## Slide 2: Characteristics of selected wireless links
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
5-11
54
802.11b
802.11a,g
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)

## Slide 3: Wireless Link Characteristics
important differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices (motors) interfere as well
  multipath propagation: radio signal reflects off objects ground, arriving ad destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 4: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 5: IEEE 802.11 Wireless LAN
802.11b
2.4-5 GHz unlicensed spectrum
up to 11 Mbps
direct sequence spread spectrum (DSSS) in physical layer
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antennae
  2.4-5 GHz range
  up to 200 Mbps
all use CSMA/CA for multiple access
all have base-station (infrastructure mode) and ad-hoc network versions

## Slide 6: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router

## Slide 7: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  AP has a name (SSID) and MAC address
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  may perform authentication
  will typically run DHCP to get IP address in AP’s subnet

## Slide 8: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 9: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 10: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS (Distributed Inter-frame Space) then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle, stops otherwise
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (Short Inter-frame Spacing)(ACK needed due to hidden terminal problem)

## Slide 11: Hidden Terminal Example
H1 is transmitting a frame and halfway through H1’s transmission, Station H2 wants to send a frame to the AP.
H2, not hearing the transmission from H1, will first wait a DIFS interval and then transmit the frame, resulting in a collision.
The channel will be wasted during the entire period of H1’s transmission as well as during H2’s transmission.

## Slide 12: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to AP using CSMA
  Indicates the total time required to transmit the DATA frame and the acknowledgment (ACK) frame
  RTSs may still collide with each other (but they’re short)

## Slide 13: Avoiding collisions (more)
BS broadcasts clear-to-send CTS in response to RTS
CTS frame:
  gives the sender explicit permission to send
  instructs the other stations not to send for the reserved duration.
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!

## Slide 14: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 15: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: Source MAC address
of wireless host or AP transmitting this frame
Address 1: Destination MAC address
of wireless host or AP
Address 3: MAC address
of router interface to which AP is attached
Address 4: used only in ad hoc mode

## Slide 16: 802.11 frame: addressing
Sending a datagram from the router interface R1 to the wireless Station H1:
  ARP to determine the MAC address of H1
  Sends Ethernet Frame: Source MAC: R1, Dest MAC: H1
AP: 802.3802.11
Address1: H1 MAC, Address2: AP MAC, Address3=R1 MAC

## Slide 17
Internet
router
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing
Sending a datagram H1 to the router interface R1

## Slide 18
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for RDT) (Reliable Data Transmission)
frame type
(RTS, CTS, ACK, data)
802.11 frame: more

## Slide 19: Data Link Layer Part VI: IEEE 802.11 wireless LANs (“Wi-Fi”)