## Slide 1: QUEUING ANALYSIS

## Slide 2: Overview
This is a summary of the Queuing Theory Notes on ODTU CLASS
READ THE QUEUING THEORY NOTES

## Slide 3: System: Parameters, Metrics
l
l
l
We want to find  Metrics: E[Ns], E[Ts],E[NQ], E[TQ]
GIVENParameters: , 
System: Queue+Server
Assumptions:
Infinite Buffer Space
< 

## Slide 4: System State
The System State: The number of packets in the system at any time
The expected number of packets in the system at steady state
:The steady state probability that the system is at state i (has i packets)

## Slide 5: Change of System State
Arrival change state from state i to i+1
Departure change state from state i to i-1
0
1
i
i-1
i+1
Arrival
Departure
Arrival
Arrival
Arrival
Departure
Departure
Departure

## Slide 6: Change of System State
Watch the system’s any state i long enough time T
  Niup:# of times state i goes up to i+1 Average state transition rate from i to i+1=
  Niup /T=  transitions per second
  Nidown:# of times state i goes down to i-1=
  Average state transition rate from i to i-1= Nidown /T=  transitions per second

## Slide 7: Change of System State
Define average time to change state from state i to i+1=1/ sec/change
Define average time to change state from state i to i-1=1/ sec/change

## Slide 8: Queue Analysis with Markov Chain
IF: State transition times are exponentially distributed
  Inter-arrival times are exponentially distributed with average of 1/λ
  Service times are exponentially distributed with average of 1/  Packet sizes are exponentially distributed
  Markov Processes (memoryless)
0
1
i
i-1
i+1
λ
μ
λ
λ
μ
μ
λ
μ

## Slide 9: Queue Analysis with Markov Chain
Balance at the steady state:
Total Rate of going into a state = Total rate of leaving the state
0
1
i
i-1
i+1
λ
μ
λ
λ
μ
μ
λ
μ

## Slide 10: Queue Analysis with Markov Chain
Balance at the steady state:
Total Rate of going into a state = Total rate of leaving the state
Using the state definitions and the balance equations (Proof is on METUCLASS -included in class content) :
  Probability that the system is empty:
  Probability that the system has i packets:

## Slide 11: Queue Analysis with Markov Chain
What kind of queue did we analyze with the Markov Chain model? (A/B/1 in Kendall’s notation)
  Inter-arrival times are exponentially distributed with average of 1/λ
  Service times are exponentially distributed with average of 1/  Packet sizes are exponentially distributed
M/M/1 Queue:
  A: Exponential arrivals
  B: Exponential service times

## Slide 12: Queue Analysis with Markov Chain
M/M/1 Queue:
  E[Ns]= /(1- ) (ONLY for M/M1)
   E[NQ]=E[Ns]- = 2/(1-)=
  E[Ts]= E[Ns]/ =1/ - Little’s Law (for all queuing systems including M/M/1 where there are no packet losses)

## Slide 13: M/M/1 Queue: Response Time vs. Arrivals
For some , 

## Slide 14: Exponential Distribution
We say that a random variable X is distributed exponentially with rate :
X~Exp()
if X has the probability density function:
f(x)= e- x, x0
0 otherwise

## Slide 15: Exponential Distribution
E[X]=1/
Var[X]= 1/2
Note:  referred to as the rate of the distribution because the mean of the distribution is 1/ 

## Slide 16: Exponential Distribution
Exponential distribution is memoryless:
  Let X~Exp()
  P(X>s+t | X>t)=P(X>s)
  The probability that you wait for at least another s seconds for the bus is the same as:
  The probability that you just came to the bus stop and wait for s seconds before the bus comes.
  Independent of t
Example:
  Let X show the waiting time for a bus
  You waited for the bus for t seconds

## Slide 17: Poisson Process
Consider a stochastic counting process N(t)
N(t) represents the total number of events in [0, t]
N(0)=0
t > 0, N(t)>=0

## Slide 18: Poisson Process
A Poisson process with rate l is a sequence of events
The number of events that occur in disjoint intervals are independent
The number of events in any [t, t + t] is Poisson distributed with parameter lt
λ is the rate of the process as E[N(t)]= λt.

## Slide 19: Poisson Process
Times between the events are random variables with the following properties:
  Independently and identically distributed
    (i.i.d: each random variable has the same probability distribution as the others and all are mutually independent.)
  exponentially distributed with rate λ
    exponentially distributed  number of events over interval [t,t+x] is Poisson distributed

## Slide 20: M/M/1 Queue Summary
M/M/1 Queue is a queue with Poisson arrivals (exponentially distributed interarrival times) and exponentially distributed packet sizes!
  E[Ns]= /(1- )
  E[NQ]=E[Ns]- = 2/(1-)
  E[Ts]= E[Ns]/ =1/ (- )Little’s Law

## Slide 21: Poisson Process Properties
If arrivals to single server with exponential service times are Poisson with mean , departures are also Poisson with mean , if (<)
  Remember: Departures are always with mean  if <1 (Throughput X=)
l
l
1
l
2
<1
<2

## Slide 22: Properties of Poisson Process
If two or more independent Poisson process A1 , ..., Ak are merged into a single process A = A1 + A2 + ... + Ak , the process A is also Poisson with a rate equal to the sum of the rates of its components
A1
Ai
Ak
A
independent Poisson processes
Poisson process
merge
l1
li
lk

## Slide 23: Properties of Poisson Process
If a Poisson process A is split into two other processes A1 and A2 by randomly assigning each arrival to A1 or A2 , processes A1 and A2 are Poisson
A1
A2
A
Poisson processes
Poisson process
split randomly
l1
l2
with probability p
with probability (1-p)

## Slide 24: Examples

## Slide 25: Example
An M/M/1 packet transmission system has an arrival rate l packets/sec. Assume that the arrival rate is increased from l to k l , k>1. At the same time (keeping the packet length distribution unchanged), the transmission capacity is increased by a factor of k.
Result:
Only per packet delay is decreased. An arriving packet
sees the same (average) # of pkts in the queue but
they are moving k times faster.

## Slide 26: Queuing System Application Multiplexing Traffic
A link may carry several traffic streams multiplexed
Assume that
  m statistically identical and independent Poisson packet streams with an arrival rate of l/m are transmitted over a communication line
  The packet lengths for all streams are independent and exponentially distributed, and the average transmission time is 1/m
Channel Allocation Mechanism affects the average packet delay
  Statistical Multiplexing
  Static Allocation

## Slide 27: Queuing System Application Multiplexing Traffic
Statistical multiplexing
  Packet streams are merged into a single Poisson stream with rate l and transmitted on FCFS basis
Static allocation (Time- and Frequency-division multiplexing, TDM/FDM)
  The transmission capacity is divided into m equal portions, each of which is an M/M/1 queue
Which one do you think gives faster (on average) service?

## Slide 28: Queuing System Application Multiplexing Traffic
Statistical multiplexing
  Packet streams are merged into a single Poisson stream with rate l and transmitted on FCFS basis
l/m
l/m
l/m
l

## Slide 29: Queuing System Application Multiplexing Traffic
Static allocation (Time- and Frequency-division multiplexing, TDM/FDM)
  The transmission capacity is divided into m equal portions, each of which is M/M/1 queue
l/m
l/m
l/m

## Slide 30: Queuing System Application Example 1

## Slide 31: Queuing System Application Example 1 Solution
Server 1: TDM: Server is used by 3 connections
  Assumption: TDM preserves Poisson merging
  Each Connection sees a separate M/M/1 queue system
  µ1=2.5p/s 1= 1/2.5=0.4
  µ2=µ3=1.25p/s 2=3=1/1.25=0.8
  Server behaves like a server with 1 (0.4) 50% of the time, a server with 2 (0.8) 25% of the time, a server with 3 (0.8) 25% of the time
  E[Nserver]=0.4*0.5+0.8*0.25+0.8*0.25=0.6

## Slide 32: Queuing System Application Example 1 Solution
Server 1: TDM: Server is used by 3 connections: All queues are isolated:
  E[NQ1]= 12/(1-1)=0.16/0.6
  E[NQ2]= 22/(1-2)=0.64/0.2
  E[NQ3]= 32/(1-3)=0.64/0.2
  E[Ns]=E[NQ1]+E[NQ2]+E[NQ3]+E[Nserver]
  =0.16/0.6+0.64/0.2+0.64/0.2+0.6=43.6/6

## Slide 33: Queuing System Application Example 1 Solution
Server 2: SM, all connections see the same server, share the same queue
µserver2=120/20=6p/s
Total=3p/s
=0.5 E[Ns]= /(1- )=1
TOTAL=43.6/6+1

## Slide 34: Queuing System Application Example 1 Solution
E[TS] for connection 1=E[TSTDM]+E[TSSM]
=1/(µ1-1)+1/(µserver2-Total)
=1/(2.5-1)+1/(6-3)=1sec

## Slide 35: Example 2
Repeat the analysis in class for M/M/1/N (Finite buffer with N buffers)
Write the balance equations: rate in rate out
Find the limiting probabilities: i
Find 0 using i=1 (FINITE SUM)
Probability of a packet loss: Probability of a packet arriving and finding the system with N packets: N
0
1
N-1
2
N
λ
μ
λ
λ
μ
μ

## Slide 36: More Exercises

## Slide 37: Queuing System Exercise Example 3
A 50 kbps line is used to support 10 sessions each generating poisson traffic at a rate of 150 packets/min. Packet lengths are exponentially distributed with mean 1000 bits. For each session:
a) find the average # of packets in the queue and the average delay per packet when i) TDM and ii) SM is used
a-i) TDM: All sessions behave like separate queuing system For each session: =150/60=2.5 pkts/sec
  Server capacity per queue=50 kbps/10=5kbps
  =5000bits/sec=5 pkts/sec
  utilization  =2.5/5=0.5
  E[NQ]=2/(1-)=0.5 per queue10x0.5=5 for all queues
  E[Ts]=1/(-)=0.4 seconds per packet

## Slide 38: Queuing System Exercise Example 3
a-ii) SM: Single queue
For each session: l=150/60=2.5 pkts/sec
arrival rate=Sl=10l=10x2.5 pkts/sec=25 pkts/sec
line capacity=50 kbps=50000bits/sec
m=50 pkts/sec
utilization r=25/50=0.5
A 50 kbps line is used to support 10 sessions each generating poisson traffic at a rate of 150 packets/min. Packet lengths are exponentially distributed with mean 1000 bits. For each session:
a) find the average # of packets in the queue and the average delay per packet when i) TDM and ii) SM is used
  E[NQ]=2/(1-)=0.5 for the single queue
  E[Ts]=1/(-)=0.04 seconds per packet

## Slide 39: Queuing System Exercise Example 3
A 50 kbps line is used to support 10 sessions each generating poisson traffic at a rate of 150 packets/min. Packet lengths are exponentially distributed with mean 1000 bits. For each session:
b) if 5 of the session generate traffic with rate of 250 pkts/min and other 5 with 50 pkts/min, find the average # of packets in the queue and the average delay per packet when i) TDM and ii) SM is used
b-i) TDM:
For each session with 250 pkts/min: l=250/60 pkts/sec
line capacity per queue =50 kbps/10=5kbps=5000bits/sec, m=5pkts/sec
  utilization r=250/60*1/5=0.833
E[NQ]=2/(1-)=4,158 per queue
For each session with 50 pkts/min: l=50/60 pkts/sec
r=50/60*1/5=0.166  E[NQ]=0.033 per queue
5(4.158+0.033)=20.95  for all queues

## Slide 40: M/M/1 Queuing System: Exercise
Customers arrive at a fast-food restaurant as a Poisson process with an arrival rate of 5 per min
Customers wait at a cash register to receive their order for an average of 5 minutes
Service times to customers are independent and exponentially distributed
What is the average service rate at the cash register? (Answer: 5.2)
If the cash register serves 10% faster, what is the average waiting time of customers? (Answer: 1.39min)

## Slide 41: SUMMARY

## Slide 42: Summary
System parameters:
  Average arrival rate:  (packets/second)
    =1/average interarrival time
    depends on traffic pattern
  Average service rate:  (packets/second)
    =1/expected service time=1/E[S]
    E[S]=average packet size/line rate
    depends on packet size distribution
  Number of servers
  We always assume FCFS
<
l

Queue
Server
System

## Slide 43: Summary
Performance metrics
  E[Ns], E[NQ], E[Ts], E[TQ]
  Utilization (U or )=fraction of busy time
  By definition:
    Probability that the server is busy=Utilization
    Probability that the system is idle=1-Utilization
  If there are no packet losses =/
  Packet losses can happen:
    If  finite or infinite buffer space
    Finite buffer space

## Slide 44: Summary
Utilization example: 4 packets served on the outgoing line with C bps capacity. Assume 4 is a large enough number to have averages.
P1
P2
P3
P4
Observation time: T
IA1
IA2
IA3
IA4
S1
S2
S3
S4

## Slide 45: Summary
Pi: Size of packet i in bits.
Si: Service time for packet i. S= Pi/C
IAi: Interarrival time for packet I
X=Output line can be used to show the arrivals
P1
P2
P3
P4
Output line during observation time: T
IA1
IA2
IA3
IA4
S1
S2
S3
S4
=

## Slide 46: Summary
Note that during T, < all the time
What do you say for the queue size during T?
Draw a scenario where > during some part of T but on the average <
P1
P2
P3
P4
Observation time: T
IA1
IA2
IA3
IA4
S1
S2
S3
S4

## Slide 47: Summary
Performance metrics
  Throughput (X)=Rate of completion of packets
  Note that X being able to serve at a certain rate does not mean that there are packets to serve
  X=U.  Given that there are packets the server can serve at rate 

## Slide 48: Summary
Little’s Law:
  Only assumption: what goes in goes out
  E[Ns]=E[Ts]. 
  Valid for:
    Any number of servers, any service order (doesn’t have to be FCFS), any arrival and service statistics
l
l
l
What goes in goes out no losses

## Slide 49: Summary
l
l
l
E[Ns]= E[Ts]
Little’s Law
l
l
l
E[NQ]= E[TQ]
l
l
l
E[NServer]= E[TinServer]
=E[S]=/

## Slide 50: Summary
For infinite and stable queues:
  What goes in goes out
  Throughput X=
  Define: =/
  Utilization U==/

## Slide 51: Summary
M/M/1 queues:
  Interarrival times are exponentially distributed
  Service times are exponentially distributed at fixed line rate, packet sizes are exponentially distributed
Performance:
  Markov Chain Model:
    Prob that the system is idle:0=1-
    Prob that there are i packets in the system I =(1-) i
    E[Ns]= /1-   E[NQ]=E[Ns]- 
    E[Ts]= E[Ns]/ =1/ - Little’s Law
    E[TQ]=E[Ts]-E[S]

## Slide 52: QUEUING ANALYSIS