## Slide 1: Transport Layer Part I

## Slide 2: Where are we now?
Introduction to Networking
Basic Queuing Theory
Application Layer
Transport Layer
Network Layer and Routing
Data Link Layer
Medium Access Control SubLayer
Physical Layer
Further subjects (we will decide what to talk about based on the time left at the end of the semester)

## Slide 3: Layered Architecture: Application Layer
Application: Firefox
Application data: Jpeg image, HTML text
Application layer protocol: HTTP
  Defines the rules to communicate the application data between the processes
Application layer:
  needs the HTTP messages to be transmitted from sender process to receiver process
  Gives the HTTP messages to the transport layer
process
Ankara
process
host or
server
Internet
controlled by
app developer
host or
server
Pittsburgh
application
transport
application
transport

## Slide 4: Layered Architecture: Transport Layer
Transport layer protocol: TCP
  Encapsulates application layer messages in segments
  Transmits the data from sender process to receiver process
Transport layer:
  Needs the segments to be transmitted from sender host machine to receiver host machine
  Gives the segments to the network layer
process
Ankara
process
host or
server
Internet
controlled by
app developer
host or
server
Pittsburgh
application
transport
network
application
transport
network

## Slide 5: Encapsulation
source
application
transport
network
segment
datagram
destination
application
transport
network
message
Network cloud
User data
D
HA
D
HT
HA
D
HT
HA
D
HN
HA
D
HT
HA
D
HT
HA
D
HN
D
The communicated units at a certain layer have different names
If this name is not specifically necessary we will just call the communicated unit a packet
Notes: 5

## Slide 6: What do we need to know about network layer at this point
Transport layer vs. network layer:
  transport layer: logical communication between processes
  network layer: logical communication between hosts
  the most common network layer protocol : Internet Protocol (IP)
  Carries IP datagrams
  The hosts are identified by IP addresses:
    Example: 144.122.199.90

## Slide 7: What do we need to know about network layer at this point
Internet Protocol (IP)
  Can deliver the transport layer segments from the source host to the destination host
    No guarantee of delivery  Datagrams can be lost
  Connectionless communication:
    No signalling phase before data transmission
    Datagrams that carry the parts of the same user data can be sent over different paths and devices
    Datagrams can be delivered out of order
    No state information to keep track of what is sent or received

## Slide 8: Internet transport-layer protocol services
Service primitives:
  Implemented as the Socket Data Structure member functions
  Application programmers can write code according to a standard set of primitives and have these programs work on a wide variety of networks
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 9: Remember: Sockets
Socket:
Process addressing
Process interface to the network
Data mux out of single physical interface from many processes
Data demux from single physical interface to many processes

## Slide 10: Transport Layer Segment
IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
Port numbers are components of process IDs
Host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 11: Transport Layer Protocols
UDP
  No state on either side Connectionless
TCP
  State at both sides Connection-oriented
  State: which segments are sent, which segments are received, order of segments
Run on sender and receiver host devices

## Slide 12: Connectionless demultiplexing
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 13: UDP: User Datagram Protocol
“no frills,” “bare bones” Internet transport protocol
Only provides process demux via socket
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 14: UDP: more
often used for streaming multimedia apps
  loss tolerant
  rate sensitive
other UDP uses
  DNS
reliable transfer over UDP: add reliability at a higher layer
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 15: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 16: The Real-Time Transport Protocol
A layer between UDP (Transport Layer) and application layer
Adds more features to UDP without delays of TCP
The position of RTP
in the protocol stack.
Packet nesting.

## Slide 17: The Real-Time Transport Protocol
Provides end-to-end delivery services for data with real-time characteristics, such as interactive audio and video.
Those services include payload type identification, sequence numbering, timestamping and delivery monitoring.

## Slide 18: Internet transport-layer protocol services
Service primitives:
  Implemented as the Socket Data Structure member functions
  Application programmers can write code according to a standard set of primitives and have these programs work on a wide variety of networks
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 19: Use of service primitives
Server 1 and Server 2 are 2 server processes on host 2
Server 1: time of day server process
  Attaches itself to port 1522
  LISTEN: Waits for an incoming call
App is a a client process on host 1
  wants to find out the time-of-day
  CONNECT: source port 1208, dest port 1522

## Slide 20: Use of service primitives
A transport connection is established between the application process on host 1 and server 1 on host 2.
Client processSEND: sends a request for the time
The time server process RECEIVE, SEND: responds with the current time
DISCONNECT: The transport connection is then released.

## Slide 21: Use of addresses and service primitives
How does the client process on host 1 know that the time-of-day server is attached to port 1522?

## Slide 22: Client Connection to Port
  Know address ahead of time
    e.g. collection of network device stats
  Well known addresses
    Web at port 80, mail at port 25
  Name server (at a well-known port)
    a user sends a message specifying the service name, and the name server sends back the port address (Similar idea as in DNS)

## Slide 23: Sending: Transport Layer Mux (TCP/UDP)
Host uses Destination IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 24: Receiving: TCP Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
receiving host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 25: Connection-oriented demux (cont)
Client
IP:B
P1
client
IP: A
P1
P2
P4
server
IP: C
SP: 1208
DP: 1522
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B
delivering received segments
to correct socket
Demultiplexing at rcv host:
gathering data from multiple sockets, enveloping data with header (later used for demultiplexing)
Multiplexing at send host:
Time server process
Web server processes

## Slide 26: TCP: Transport Control Protocol
End-to-end between source and destination nodes:
  Connection-oriented
  Reliable delivery
  Flow Control
  Congestion control
Problem: Underlying network that actually carries the messages end to end is unreliable and connectionless!

## Slide 27: Transport Layer Socket/Port summary
Client
IP:B
P1
client
IP: A
P1
P2
P7
server
IP: C
DP: 53
DP: 53
P8
P3
D-IP:C
D-IP: C
SP: 5775
DP: 80
D-IP:C
S-IP: B
DNS process over UDP
Web server processes over TCP
Client process initiates the connection with the server process
Client process must know the server process address: IP address and Transport layer port  That is all UDP socket!
Transport layer port on the server side: Fixed, well known or can be looked up from some table

## Slide 28: Transport Layer Socket/Port summary
Client
IP:B
P8
client
IP: A
P1
P2
P7
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B
Time server process
Web server processes
TCP Sockets require 4 tuple.
Both client and the server need to keep state of the specific process.
Sockets on the same client that connect to the same server and same port has different local ports to differentiate
P4
P9
SP: 1208
DP: 1522
S-IP: A
D-IP:C
Web server process

## Slide 29: Transport Layer Part I