## Slide 1: Techniques for Reliable Data Transmission

## Slide 2: Motivation
Providing
  Reliable packet delivery
  Flow Control
  Congestion control
Problem: Underlying transmission facilities that actually carry the messages is unreliable!
  Bit errors, corrupt packets
  Lost packets

## Slide 3: Motivation
Transport layer (TCP):
  End-to-end process communication over unreliable connectionless network
Data Link layer (later)
  Communication between two machines connected by an unreliable link with errors
Upper Layer
Reliable Transmission
Layer
Data
Data
Control
Unreliable Transmission

## Slide 4: Basics
The sender wants to check
  if receiver got the transmitted segments
  If the sending rate is appropriate
Receiver acknowledges (ACKs) that it got the segments
Provides:
  Reliable transport
  flow control
  feedback related to the current congestion state of the network

## Slide 5: How do ACKs work
Special packets sent by the receiver back to the sender with the information:
  The packet is/ packets are received correctly
  Expecting next packet(s)
Data communication is mostly two-way: Receiver piggybacks the ACK information on its user data
Data unit 1
ACK2: I got Data unit 1
I expect Data unit 2
Data unit
ACK
Data unit

## Slide 6: How do ACKs work
If sender receives the ACKs goes on transmitting
If sender fails to get the ACKs decides that something is wrong and retransmits to ensure reliable delivery
Data unit 1
ACK2
Data unit 2
Data unit 2

## Slide 7: Issues
When does the sender fail to get an ACK?
  The sender data does not reach the receiver, gets lost The receiver doesn’t get it, doesn’t send an ACK
  Sender is too fast for the receiver, sender data reaches the receiver but it gets drowned in packets  The receiver loses packets, doesn’t send an ACK
  Receiver sends an ACK but it gets lost on the way

## Slide 8: Ideal Network
Assumptions:
  Error free transmission
  Infinite buffer at the receiver / There is no processor limit
Any reason to lose packets?
  No acknowledgment is necessary
This is basically the definition of no flow control for one-way communication

## Slide 9: Some Flow Control Algorithms
Stop and Wait
Sliding window with Go Back N
Sliding window with Selective Repeat

## Slide 10: Stop and Wait when everything is OK 
Source transmits packets
Destination receives packets and replies with ACK
Source waits for ACK before sending next packet
Destination can stop flow by not sending ACK
Works well for a few large packets
Simple
Receiver side
Sender side
time

## Slide 11: Stop and Wait: Timing Details
tdata: time to transmit the data packet out of the sender interface
tsr: time until the data packet reaches the receiver
tack: time to transmit the ack packet out of the receiver interface
trs: time until the ack packet reaches the sender
RTT= tsr + trs
tproc: time to process the data at the receiver and the ack at the sender. Can be ignored.
tdata
trs
tsr
tack
tproc

## Slide 12: Stop and Wait: Efficiency
T=Total time spent for one data packet
T=tdata+tsr+tack+trs
The actual time spent for the data transmission: tdata
Efficiency (): Fraction of time that is spent directly for the user data
tdata
trs
tsr
T
tack
tproc

## Slide 13: Stop and Wait: Efficiency
Efficiency (): Fraction of time that is spent directly for the user data
=tdata/(tdata+tsr+tproc+tack+trs+tproc)
Small enough terms can be ignored:
  tproc
  tack
=tdata/(tdata+tsr+trs)
tdata
trs
tsr
T
tack
tproc

## Slide 14: Stop and Wait for transmission with errors and losses
Errors on transmission line
Network nodes between sender and receiver can lose packets
Finite buffer at the receiver / Processor limit
Sender does not get ACK because:
  Buffer overflow at the receiver
    Buffer overflow may happen at the receiver when the sender sends packets at a rate faster than the receiver
  Data packets or acknowledgement packets are lost/ in error

## Slide 15: ARQ Error Control
Types of errors: Lost packets, damaged packets
Error control schemes that involve error detection and retransmission of lost or corrupted packets are referred to as Automatic Repeat Request (ARQ) error control

## Slide 16: Summary of Techniques using ACKs
Individual or piggybacked cumulative ACKs
Pipelining
  Sender Window>1, Receiver Window>1
Sequence numbering
Retransmissions triggered by:
  Time out: If ACK is not received until a certain time
  Duplicate ACK: If ACK for the same data is received multiple times without a new ACK
  NACK

## Slide 17: Stop and Wait for transmission with errors and losses
Sender transmits packets one by one
Keeps timeout for every packet transmitted
Waits for ACK
If received packet is damaged or lost
  No ACK is sent
  Timeout expires, sender retransmits
Data: A
ACK
Data: B
ACK
Data: C
ABCD
Timeout
Data: C
ACK
Data: D
ACK
ABCD
Automatic Repeat reQuest
(ARQ) protocol!

## Slide 18: Stop and Wait for transmission with errors and losses
What happens if ack is damaged or lost
  Data packet is correctly transmitted
  Timeout expires, sender retransmits
What is the problem here
  Receiver thinks the transmitter will send the next packet (it sent an ack)
  Transmitter sends the same packet
Data: A
ACK
Data: B
ACK
Data: C
ABCD
Timeout
Data: C
ACK
Data: D
ACK
ABCCD
Automatic Repeat reQuest
(ARQ) protocol!
ACK

## Slide 19: Stop and Wait for transmission with errors and losses
Use sequence numbers for data packets and ACKs
ACK n: Receiver acks upto data packet number n-1 and expects data packet n
If receiver gets two copies of the data packet (duplicate)  discards
Packet 0
Data: A
ACK1
ACK2
ABCD
Timeout
ACK3
ACK4
ABCD
ACK3
Packet 1
Data: B
Packet 2
Data: C
Packet 2
Data: C
A1
P0 is ok
P1 expected
Starts with P0
Expects A1 to send P1
Packet 3
Data: D
Expects P3
gets P2 instead
discards it
x
A2
P1 is ok
P2 expected
A2
P2 is ok
P3 expected

## Slide 20: Stop and Wait for transmission with errors and losses
We can solve this with 1-bit sequence number (mod 2)
Why does it work?
Packet 0
Data: A
ACK1
ACK0
ABCD
Timeout
ACK1
ACK
ABCD
ACK1
Packet 1
Data: B
Packet 0
Data: C
Packet 0
Data: C
A1
P0 is ok
P1 expected
Expects A1 to send P1
Packet 1
Data: D
Expects P1
gets P0 instead
discards it
x
A0
P1 is ok
P0 expected
A1
P0 is ok
P1 expected

## Slide 21: Efficiency of Stop and Wait
Example: (Large bandwidth x delay channels)
50Kb/s satellite link, RTT=500ms, packet=1000 bits
t=0 send
t=20 packet sent
t=270 packet is at receiver
t=520 ACK is back
 Efficiency=20/520
Sender is busy for 20/520 = 4% of time ... very inefficient.

## Slide 22: Solution: Pipelining
A
B
99
data stream
51
50
49
1
0
ACK stream
PROBLEM with Stop and Wait : Sender has to wait until a packet is acked before sending the next packet.
Pipelining:
Allowing several packets into the network before receiving ACK
keeps the transmission line from being idle !

## Slide 23: Efficiency of Stop and Wait
Example: (Large bandwidth x delay channels)
50Kb/s satellite link, RTT=500ms, packet=1000 bits
t=0 send
t=20 packet sent
t=270 packet is at receiver
t=520 ACK is back
Solution: Allow sender to send up to w (>1) packets without waiting for ack.
So from t = 0 to t = 520, sender could have sent 26 packets, so let w should be at least 26.

## Slide 24: Sliding Window Flow Control: Sender
Sender has a (buffer) window of WS contiguous packets
At any given time sender only knows about the packets in the window
Sender can transmit/retransmit the packets in the window
0
1
2
3
Sender WS=4
4
5
6
7
New packets that are allowed in the window come from the upper layer
Each packet is numbered (sequence number)
Packets arrive from upper layer

## Slide 25: Sliding Window Flow Control: Sender
When Ack2 comes Packet 1 goes out of the window
Window moves to include next packet from the upper layer (Packet 5)
0
1
2
3
Ack1
4
Ack2
Sender WS=4
5
Initially:
  Window has 0 to WS-1 (0 to 3)
  The transmitter can send WS packets
When Ack1 comes Packet 0 goes out of the window
Window moves to include next packet from the upper layer (Packet 4)

## Slide 26: Sliding Window Flow Control
With a sender window size of 1
  the sender waits for an ACK before sending another packet
  Which protocol is this actually?
  This protocol behaves identically to stop and wait

## Slide 27: Duplex Protocols
Usually data flows both directions
Ex: HTTP request response
Piggy backing :
  Send data and the acknowledgement for the received data together
  We can use the header of the packet to denote if it is an acknowledgement packet or a data packet.
Cumulative acknowledgement:
  ACKn acknowledges all upto n-1
  It is possible to send ACK5 after ACK3 without sending ACK4

## Slide 28: Sliding Window Protocols Piggybacking Cumulative Acknowledgements
Ack2: Cumulative ACK: Acks all packets upto and including 1 (packet 0 and packet 1)
0
1
2
3
4
Ack2 on data
Sender WS=4
5
6

## Slide 29: Sliding Window Protocols Piggybacking Cumulative Acknowledgements
Ack3: Acks all packets upto and including 2 (only packet 2)
Window moves
0
1
2
3
4
Ack2 on data
Sender WS=4
5
Ack3 on data
6

## Slide 30: Sliding Window Protocols Piggybacking Cumulative Acknowledgements
0
1
2
3
4
Ack4
with data
Sender WS=4
5
Long propagation delay pipe is not full
6
7

## Slide 31: Sliding Window Protocols Definitions
Sequence Number: Each packet is assigned a k-bit sequence number that is incremented as each packet is transmitted.
  Range of sequence number is [0..2k-1],
  i.e.,packets are counted modulo 2k
  How to determine the sequence number range?

## Slide 32: Sliding Window Protocols Definitions
Sender’s Window: Keeps sequence numbers of packets that have been sent (or can be sent) but not yet acknowledged
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Sent but not acked
Sent and acked
Sender is done with these packets
Can be sent without getting a new ack
WS
Example with 3 bit sequence numbers, Ws=7

## Slide 33: Sliding Window Protocols Definitions
Piggybacked cumulative Ack 0 comes
Window moves
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Sent but not acked
Sent and acked
Sender is done with these packets
Can be sent without getting a new ack
Sender goes on sending packets
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
WS

## Slide 34: Sliding Window Flow Control: Receiver
Receiver has a (buffer) window of WR contiguous packets
At any given time receiver only knows about the packets in the window
Window contains packets that are already accepted and can be accepted
0
1
2
3
Receiver WR=4
4
5
6
7
Receiver delivers contiguous groups of received packets to the upper layer
These packets go out of the window

## Slide 35: Sliding Window Protocols Definitions
Receiver’s Window: Keeps sequence numbers of packets that have been received (or can be accepted) but not yet delivered to the upper layer
WR is not necessarily the same as WS
Progresses independent of the sender window progress
Acked and delivered to the upper layer
Receiver is done with these packets
Can be accepted if received
WR
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Any packet which falls outside the receiver window is discarded at the receiver
Example with 3 bit sequence numbers

## Slide 36: Sliding Window Protocols Definitions
Upper layer reads two more packets
Receiver is done with these packets, receiver window moves
Can be accepted if received
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
WR
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
WR

## Slide 37: Automatic Repeat Request (ARQ)
What if a data or ACK packet is lost when using a sliding window protocol?
  Sliding Window with Go back N
  Sliding Window with Selective Repeat (Selective Reject or Retransmission)

## Slide 38: Sliding Window with Go Back N: Basics
Sender window size> 1 Pipelining, multiple packets in transmit
Receiver window size = 1Only accepts one packet
If packet is received without any error ACK as usual with next packet expected
Else
  Discard that packet and all future packets until error/lost packet received correctly
  Transmitter must go back and retransmit that packet and all subsequent packets

## Slide 39: Go Back N: Retransmission Idea 1
10
0
1
2
3
4
5
6
7
8
2
3
4
5
6
7
8
9
10
0
1
2
3
4
5
6
7
8
9
E
D
D
D
D
D
D
discarded by
receiver
packet with
error
timeout interval
ACK 1
ACK 2
ACK 3
ACK 4
ACK5
ACK6
ACK 7
ACK 8
Time
sender
receiver
The sender maintains a timer for each packet that is sent but unacked.
If there are a lot of errors the sender will retransmit a lot of packets.

## Slide 40: Go Back N: Retransmission Idea 2
Sender gets duplicate ACK and understands packet 2 was not received
Sender retransmits packet 2 before it times out
Saves time and does not waste the bandwidth for packets that will be discarded anyway
0
1
2
3
4
5
6
2
3
4
5
6
7
8
9
10
0
1
2
3
4
5
6
7
8
9
E
D
D
D
D
discarded by
receiver
packet with
error
ACK 1
ACK 2
ACK 3
ACK 4
ACK5
ACK6
ACK 7
ACK 8
Time
sender
receiver
ACK 2
ACK 2
ACK 2
ACK 2

## Slide 41: Sliding Window with Go Back N: Sender
k-bit seq # in pkt header
“window” of up to N, consecutive unACKed pkts allowed

## Slide 42: Go Back N Window Size and Sequence numbers
0
1
2
3
0
1
2
3
0
1
0
1
2
3
ACK 1
ACK 1
ACK 2
ACK3
ACK0
Time out
sender
receiver
2
3
ACK 2
ACK 3
ACK 0
receiver
expects
1
2
3
0
Receiver cannot differentiate that
these are retransmissions
accepts Duplicate data
WS: Sender window size
Rnext: The sequence number of the next packet that the receiver expects
m: Number of bits for the sequence number
Scenario 1: m=2 and Seq numbers: 0,1,2,3, WS =4
All ACKs are lost

## Slide 43: Go Back N Window Size and Sequence numbers
0
1
2
0
1
2
3
0
1
0
1
2
3
ACK 1
ACK 1
ACK 2
ACK3
ACK0
Time out
sender
receiver
2
ACK 2
ACK 3
receiver
expects
1
2
3
Receiver differentiates that these are retransmissions
Discards but sends ACK to keep the sender going
Scenario: m=2 and Seq numbers: 0,1,2,3, WS =3
All ACKs are lost
General Case:
  WS ≤ 2m-1
  Increasing windows increase pipelining effect
0
1

## Slide 44: Sliding Window with Selective Repeat
Sender window > 1
Receiver window > 1
The sender retransmits only the packet with errors
The receiver stores all the correct packets in the receiver window that arrive following the bad one
Requires a significant amount of buffer space at the receiver
When the sender notices that something is wrong, it just retransmits the one bad packet, not all its successors
Might be combined with Negative Acknowledgment (NACK) or duplicate ACK

## Slide 45: Selective Repeat
0
1
2
3
4
5
6
7
2
8
9
10
11
12
13
14
0
1
8
9
10
11
12
13
14
E
3
4
5
6
7
2
packet with
error
ACK 1
ACK 2
ACK 9
ACK 10
ACK 11
ACK 12
ACK 12
ACK 13
Time
ACK 8
ACK 2
ACK 2
ACK 2
ACK 2
ACK 2
sender
receiver
timeout interval
Every time a receiver receives a packet, it sends an acknowledgement which contains the sequence number of the next packet expected
Example: Retransmission after 1st duplicate ACK

## Slide 46: Selective Repeat with NACK
0
1
2
3
4
5
6
7
2
8
9
10
11
12
13
14
0
1
8
9
10
11
12
13
14
E
3
4
5
2
6
7
packet with
error
timeout interval
ACK 1
ACK2
ACK 9
ACK 10
ACK 11
ACK 12
ACK 12
ACK 13
Time
sender
receiver
NACK 2
ACK 2
ACK 2
ACK 2
ACK 2
ACK 8
If some other packet is received instead, indicates this with a NACKn. This explicitly states there is something wrong with DATAn.
Duplicate ACKn: Shows all packets upto n are received contiguously. This implies there is something wrong with DATAn.

## Slide 47: Selective repeat: sender, receiver windows
Sender Window
Receiver Window

## Slide 48: Selective Repeat Window Size and Sequence numbers
0
1
2
0
0
1
0
ACK 1
ACK 1
Time out
sender
receiver
2
ACK 2
ACK 3
receiver
expects
[1,2,3]
Receiver cannot differentiate
frame 0 and accepts
Duplicate transmission
Scenario: m=2 and Seq numbers: 0,1,2,3, WR = WS =3
All ACKs are lost
[2,3,0]
[3,0,1]

## Slide 49: Selective Repeat Window Size and Sequence numbers
0
1
0
0
1
0
ACK 1
ACK 1
Time out
sender
receiver
ACK 2
receiver
expects
[1,2]
Scenario: m=2 and Seq numbers: 0,1,2,3, WR = WS =2
All ACKs are lost
[2,3]
Receiver differentiates that frame 0 is a retransmission
Discards but sends ACK to keep the sender going
General Case:
  WS =WR≤ 2m-1
  Increasing windows increase pipelining effect
Cumulative ACK2
is also possible

## Slide 50: Performance Stop and Wait no Error
bs: bits/s channel capacity on the sender link
br: bits/s channel capacity on the receiver link
P: packet size, for P=D+H (data + header)
A: ack size=H (ACK info is in the header)
RTT = tsr+trs: Round trip time
Then, the efficiency (no error case) is :
D
A
A/br
trs
tsr
T
H
P/bs
Efficiency determines the data rate available to the upper layer
Q: What is the data rate in bits/s that upper layer sees with data units of D bits?

## Slide 51: Performance Stop and Wait with error
Example:
  2 unsuccessful attempts
  Last attempt is successful
D
H
D
H
D
H
A
D
H
timeout
timeout

## Slide 52: Performance Stop and Wait with error
k: number of unsuccessful attempts
D
H
D
H
D
H
A
D
H
timeout
timeout

## Slide 53: Performance Stop and Wait
Idea: If we find an average k then we can find an average 
Average k depends on the probability of unsuccessful transmission
  P1: P{loss of data packet} P2: P{loss of ACK}
  Psuccess=(1-P1)(1-P2)
  Pfailure=1-(1-P1)(1-P2)=L
P[success at ith attempt]=(1-L)Li-1

## Slide 54: Performance Stop and Wait
  Expected number of transmissions :
  Expected number of retransmissions:
  Efficiency:

## Slide 55: Performance Stop and Wait
What is a good timeout?
D
A
A/br
trs
tsr
H
P/bs
Timeout

## Slide 56: Performance Sliding Window with Selective Repeat
Large Window:
  WP/bs >> arrival time of 1st ACK Window is not exhausted before ACK arrives
  ACKS reach sender before sender window is exhausted (to have the pipelining in full effect )
  Continuous transmission
ACK

## Slide 57: Performance Sliding Window with Selective Repeat
Line is always utilized. Efficiency is decreased due to Header and Errors
Probability of success
ACK
Fraction of Data in the packet

## Slide 58: Performance Sliding Window with Selective Repeat
Small Window:
  WP/bs << arrival time of 1st ACK
  Line is idle until ACK comes BACK
ACK

## Slide 59: Performance Sliding Window with Selective Repeat
Efficiency is decreased due to Header Errors, ACK return time
ACK
T
WP/bsr
Probability of success
Fraction of Data in the packet
Fraction of Packet Transmission in the total time spent

## Slide 60: Summary of Techniques
ACKs (individual or piggybacked cumulative)
Pipelining
  Sender Window>1, Receiver Window>1
Sequence numbering
Retransmission triggered by:
  Time out
  Duplicate ACK
  NACK

## Slide 61: Techniques for Reliable Data Transmission

## Slide 62
https://jobs.cisco.com/jobs/ProjectDetail/Cisco-Services-Network-Engineer-Graduate-Poland/1218278
bcmuratoglu@gmail.com