## Slide 1: Transport Layer Part II: TCP

## Slide 2: Where are we now?
Introduction to Networking
Basic Queuing Theory
Application Layer
Transport Layer
Network Layer and Routing
Data Link Layer
Medium Access Control SubLayer
Physical Layer
Further subjects (we will decide what to talk about based on the time left at the end of the semester)

## Slide 3: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
FLOW CONTROL:
# bytes
rcvr willing
to accept
RELIABLE XFER:
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 4: TCP reliable data transfer
TCP creates reliable service on top of IP’s unreliable service
seq # is byte-stream number of first data byte in segment
pipelined segments
cumulative ACKs
TCP uses single retransmission timer for the oldest unacked segment
retransmissions are triggered by:
  timeout events
  duplicate ACKs
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementer

## Slide 5: TCP Sender
loop (forever) {
switch(event)
event: ACK received, with ACK field value of y
if (y > SendBase) {
SendBase = y
if (there are currently not-yet-acknowledged segments)
start timer }
event: timer timeout
retransmit not-yet-acknowledged segment with the smallest sequence number
start timer
} /* end of loop forever */
Comment:
SendBase-1: last cumulatively ACKed byte

## Slide 6: TCP sender events:
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running (think of timer as for oldest unACKed segment)
expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ACK rcvd:
if acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are outstanding segments

## Slide 7: TCP: retransmission scenarios
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
time
SendBase
= 100
Host C
Seq=92, 8 bytes data
ACK=100
loss
timeout
Cumulative ACK scenario
Host D
X
Seq=100, 20 bytes data
ACK=120
time
SendBase
= 120

## Slide 8: Fast Retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs for that segment
If sender receives 3 duplicate ACKs for same data, it assumes that segment after ACKed data was lost:
  fast retransmit: resend segment before timer expires
  Does not restart the timer!

## Slide 9
Host A
Timeout for x2
Host B
time
X
resend seq X2
seq # x1
seq # x2
seq # x3
seq # x4
seq # x5
ACK x2
ACK x2
ACK x2
ACK x2
triple
duplicate
ACKs
Start timer for x2
seq# X6
DOES NOT
restart timer for x2

## Slide 10: Fast retransmit algorithm:
event: ACK received, with ACK field value of y
if (y > SendBase) {
SendBase = y
if (there are currently not-yet-acknowledged segments)
start timer
}
else {
increment count of dup ACKs received for y
if (count of dup ACKs received for y = 3) {
resend segment with sequence number y
}
a duplicate ACK for
already ACKed segment
fast retransmit

## Slide 11: Delayed Acknowledgement
TCP delays transmission of ACKs for up to 500ms
Goal: Avoid sending ACK packets that do not carry data.
  The hope is that, within the delay, the receiver will have data ready to be sent to the receiver. Then, the ACK can be piggybacked with a data segment
Delayed ACK is not used when packets arrive out of order

## Slide 12: TCP ACK generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send (possibly duplicate)
ACK, indicating seq. # of next
expected byte
Immediate send ACK, provided that
segment starts at lower end of gap
Case
1
2
3
4

## Slide 13: TCP ACK generation Example1
Initially: receiver window=[100 - 199]
t=0ms: receive segment [100 - 109]
No new segment
send ACK110 at t=150ms (delayed ACK) (Case 1)

## Slide 14: TCP ACK generation Example2
Initially: receiver window=[100 - 199]
t=0ms: receive segment [100 - 109]
t=20ms: receive segment [110 - 119]
send immediate cumulative ACK120 (Case 2)

## Slide 15: TCP ACK generation Example3
Initially: receiver window=[100 - 199]
t=0ms: receive segment [100 - 109]
No new segment, send ACK110 at t=120ms (delayed ACK)
t=140ms: receive segment [120 - 129]
send immediate duplicate ACK110 (Case 3)
t=500ms: receive segment [110 - 115]
send immediate ACK116 (Case 4)

## Slide 16: TCP Flow and Congestion Control
Problem: low capacity receiver
Solution: Flow Control
TCP Receiver tells the sender how much to send by rwnd
(b) Problem: Too much network load, high queuing delays, packet drops
Solution: Congestion Control
TCP Sender observes the ACKs to see if there is congestion by computing cwnd
rate =
w
RTT
bytes/sec
  Sender window limited by
  w=min(cwnd,rwnd)

## Slide 17: TCP Flow Control
(Suppose TCP receiver discards out-of-order segments)
spare room in buffer
RcvWindow: rcwnd
= RcvBuffer-[LastByteRcvd - LastByteRead]
Rcvr advertises spare room by including value of RcvWindow in segments
Sender limits unACKed data to RcvWindow
  guarantees receive buffer doesn’t overflow

## Slide 18: TCP Flow Control and Reliable Transfer
Window management in TCP.
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK

## Slide 19: TCP Congestion Control
goal: TCP sender should transmit as fast as possible, but without congesting network
  Q: how to find the maximum rate just below congestion level
Solution: sender limits rate by limiting number of unACKed bytes “in pipeline”:
LastByteSent-LastByteAcked  min(cwnd, rwnd)

## Slide 20: TCP Congestion Control
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
Decentralized: each TCP sender sets its own rate, based on implicit feedback:
  ACK: segment received (a good thing!), network not congested, so increase sending rate
  lost segment: assume loss due to congested network, so decrease sending rate

## Slide 21: TCP congestion control: bandwidth probing
“probing for bandwidth”: increase transmission rate on receipt of ACK, until eventually loss occurs, then decrease transmission rate
  continue to increase on ACK, decrease on loss (since available bandwidth is changing, depending on other connections in network)
ACKs being received,
so increase rate
X
X
X
X
X
loss, so decrease rate
sending rate
time
Q: how fast to increase
/decrease?
TCP’s
“sawtooth”
behavior

## Slide 22: TCP Congestion Control
How does sender perceive congestion?
loss event = timeout or 3 duplicate acks
TCP sender reduces rate (cwnd) after loss event
Mechanisms:
  Initial Rate Increase to find the available rate:
    Slow Start (exponential increase until threshold)
    Congestion Avoidance (linear increase after threshold)
  Fluctuating around the available rate: Additive Increase Multiple Decrease (AIMD)

## Slide 23: TCP Slow Start
When connection begins, cwnd = 1 MSS
  Example: MSS = 500 bytes & RTT = 200 msec
  initial rate = 20 kbps
Available bandwidth may be >> MSS/RTT
  desirable to quickly ramp up to respectable rate
When connection begins, increase rate exponentially fast until first loss event
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
Summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 24: TCP Congestion Control: more details
ACK received: increase cwnd
slowstart phase:
  increase exponentially fast (despite name) at connection start, or following timeout
  Threshold:
    Window size to Switch from exponential increase to linear increase
    Initially set, dynamically updated
congestion avoidance:
  increase linearly after threshold size is reached

## Slide 25: Noticing congestion early
After timeout event:
  cwnd instead set to 1 MSS;
  window then grows exponentially to a threshold, then grows linearly
Refinement: After 3 dup ACKs:
  cwnd is cut in half
  window then grows linearly
3 dup ACKs indicates network capable of delivering some segments
timeout before 3 dup ACKs is “more alarming”
Philosophy:
Remember: fast retransmit If sender receives 3 ACKs for the same data, it supposes that segment after ACKed data was lost, retransmits segment before timer expires

## Slide 26: TCP Congestion Control
Threshold initialized
When cwnd is below Threshold
 sender in slow-start phase, cwnd grows exponentially
When cwnd is above Threshold
 sender is in congestion-avoidance phase, cwnd grows linearly (Additive Increase Multiplicative Decrease)
When a triple duplicate ACK occurs
 threshold set to cwnd/2 and cwnd=cwnd/2, then cwnd grows linearly (TCP RENO)
When timeout occurs
 threshold set to cwnd/2 and cwnd is set to 1 MSS, then cwnd grows exponentially (Back to slow start)

## Slide 27: TCP Congestion Control

## Slide 28: TCP Congestion Control Example 1
cwnd is below Threshold
 slow-start phase, cwnd grows exponentially
cwnd is above Threshold
 congestion-avoidance phase, cwnd grows linearly
When timeout occurs
 threshold set to cwnd/2 and cwnd is set to 1 MSS, then cwnd grows exponentially

## Slide 29: TCP Congestion Control Example 2

## Slide 30: TCP throughput
Q: what’s average throughout of TCP as function of window size, RTT?
  ignoring slow start
let W be window size when loss occurs.
  when window is W, throughput is W/RTT
  just after loss (triple ack), window drops to W/2, throughput to W/2RTT.
  average throughput: .75 W/RTT

## Slide 31: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP
connection 2
Two competing sessions:
Additive increase gives slope of 1, as throughput increases
multiplicative decrease decreases throughput proportionally

## Slide 32: Fairness (more)
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  pump audio/video at constant rate, tolerate packet loss
Fairness and parallel TCP connections
nothing prevents app from opening parallel connections between 2 hosts.
web browsers do this
example: link of rate R supporting 9 connections;
  new app asks for 1 TCP, Total 10 connections, gets rate R/10
  new app asks for 11 TCPs, Total 20 connections, gets 11R/20 R/2 !

## Slide 33: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout
  unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT? how to know the real value of RTT?
Idea: Measure ACK return times

## Slide 34: TCP Round Trip Time
Q: how to estimate RTT?
Measured time from segment transmission until ACK receipt
  ignore retransmissions
ACK return times will vary, want estimated RTT “smoother”
  average several recent measurements, not just current ACK return time

## Slide 35: TCP Round Trip Time
RTT: the best current estimate of the round-trip time to the destination
TCP measures how long an ACK took (M)
Then updates RTT according to the formula
a: a smoothing factor that determines how much weight is given to the old value (Typically a = 7/8)

## Slide 36: Example RTT estimation:

## Slide 37: TCP Timeout
Upto now we estimated RTT
How to compute the timeout?
For timeout period TCP uses bRTT, but the trick is choosing b.
In the initial implementations, b was always 2, but experience showed that a constant value was inflexible

## Slide 38: TCP Timeout
Jacobson (1988) proposed b ~ std. dev. of ACK arrival time pdf
  Keep track of another smoothed variable, D, the deviation.
  Whenever an ACK is received, the difference between the expected and observed values, | RTT - M |, is computed.
  A smoothed value of this is maintained in D by the formula
RTT estimated as discussed before

## Slide 39: TCP RTT and Time out
Here,  may or may not be the same value  used to smooth RTT (typically ¾). Most TCP implementations use this
When a segment times out and is sent again, it is unclear whether the ACK is for the 1st transmission or later one
Do not update RTT on any segments that have been retransmitted.

## Slide 40: TCP RTT and Time out
Recall: Timer is restarted on 3 cases:
No acks pending, data is received from the application layer and sent. Start timer for this new segment Compute Time out from RTT estimate and Deviation
New ack is received, there are acks pending. Start timer for the oldest unacked segment Compute Time out from RTT estimate and Deviation
Time out and retransmit  Time out =2*current time out value. If there are retransmissions back to back double each time.

## Slide 41: Recall:TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 42: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  seq. #s
  buffers, flow control info (e.g. RcvWindow)
client: connection initiator
Socket clientSocket = new Socket("hostname","port number");
server: contacted by client
Socket connectionSocket = welcomeSocket.accept();

## Slide 43: TCP Connection Management
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  specifies initial seq #
  no data
Step 2: server host receives SYN, replies with SYN-ACK segment
  server allocates buffers
  specifies server initial seq. #
Step 3: client receives SYN-ACK, replies with ACK segment, which may contain data
client
server

## Slide 44: TCP Connection Management (cont.)
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
FIN
close
close

## Slide 45: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 46: Transport Control Protocol (TCP)
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 47: Transport Layer Part II: TCP