## Slide 1: Network Layer

## Slide 2: Where are we now?
Introduction to Networking
Basic Queuing Theory
Application Layer
Transport Layer
Network Layer
Data Link Layer
Medium Access Control SubLayer
Physical Layer
Further subjects (we will decide what to talk about based on the time left at the end of the semester)

## Slide 3: Layered Architecture: Application Layer
Application: Firefox
Application data: Jpeg image, HTML text
Application layer protocol: HTTP
  Defines the rules to communicate the application data between the processes
Application layer: Only exists at the end systems
  needs the HTTP messages to be transmitted from sender process to receiver process
  Gives the HTTP messages to the transport layer
process
Ankara
process
host or
server
Internet
controlled by
app developer
host or
server
Pittsburgh
application
transport
application
transport

## Slide 4: Layered Architecture: Transport Layer
Transport layer protocol: TCP/UDP
  Encapsulates application layer messages in segments
  Transmits the data from sender process to receiver process
Transport layer: Only exists at the end systems
  Needs the segments to be transmitted from sender host machine to receiver host machine
  Gives the segments to the network layer
process
Ankara
process
host or
server
Internet
controlled by
app developer
host or
server
Pittsburgh
application
transport
network
application
transport
network

## Slide 5: Layered Architecture: Network Layer
source
segment
datagram
destination
message
User data
D
HA
D
HT
HA
D
HT
HA
D
HN
HA
D
HT
HA
D
HT
HA
D
HN
D
Provides Connectivity
  the service of sending the segment from sending to receiving host
application
transport
network
application
transport
network
We will focus on the most commonly used network layer protocol: Internet Protocol (IP)
Notes: 5

## Slide 6: IP Connectionless Service
packets forwarded using destination host address
  packets between same source-dest pair may take different paths

## Slide 7: Network layer
transport segment from sending to receiving host
Addressing:
  Each device interface to network has an IP address
  Addressing hierarchically visible to the entire network
network layer protocols in every host, router
  uses the services of the Data Link Layer
network
data link
network
data link
network
data link
network
data link
l
network
data link
network
data link
network
data link
network
data link
application
transport
network
data link
application
transport
network
data link

## Slide 8: The Internet Network layer
forwarding
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 9: Two key network-layer functions
routing: determine route taken by packets from source to dest.
  routing algorithms
forwarding: move packets from router’s input to appropriate router output
analogy:
forwarding: process of getting through single interchange
routing: process of planning trip from source to dest

## Slide 10: IP Router and IP address lookup
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
IP lookup table
dest address
output link
address 1
address 2
address 3
address 4
3
2
2
1
routing algorithm determines
end-end-path through network
Table lookup
for each packet

## Slide 11: Router Packet Processing
Lookup
Address
Update
Header
Header Processing
Data
Hdr
Data
Hdr
~1M prefixes
Off-chip DRAM
Address
Table
IP Address
Next Hop
Queue
Packet
Address | Output Port-Action
A | 1, Mark high priority
B | 1
C | 2

## Slide 12: Routing Table / Forwarding Table
Routing Table
  The complete table
  Updated by the routing algorithms
  Software management
Forwarding Table
  Local sometimes partial copy of the routing table
  Look up for every packet
  Hardware management

## Slide 13: What does a Router look like?
Cisco GSR 12416
Juniper M160
6ft
19”
2ft
Capacity: 160Gb/s Power: 4.2kW
3ft
2.5ft
19”
Capacity: 80Gb/s Power: 2.6kW

## Slide 14: Router architecture overview
two key router functions:
run routing algorithms/protocol (RIP, OSPF, BGP)
forwarding datagrams from incoming to outgoing link
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware)
routing, management
control plane (software)
forwarding tables computed,
pushed to input ports
Input port and output port
on a single Line card

## Slide 15: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 16: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing

## Slide 17: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N

## Slide 18: Routers and the Layered Architecture
End systems implement the entire network stack
  Including application and transport layers
The routers implement only network layer and lower layers
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 19: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
Priority
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead
Assigned by the sender to aid in assembling the fragments of a datagram

## Slide 20: IP Addressing
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host may have multiple interfaces
  IP addresses associated with each interface
IP address: 32-bit identifier for host, router interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 21: What does a forwarding table look like?
Interface 1
Interface 2
Interface 3
IP packets carry 32 bit destination host addresses
Can the router keep track of all individual destination host addresses?
DOESN’T WORK
Address | Outgoing Interface
144.122.144.188 | Interface 1
128.2.42.10 | Interface 2
171.64.13.26 | Interface 2
144.122.150.76 | Interface 1
83.66.162.3 | Interface 3

## Slide 22: What does a forwarding table look like?
Routers keep the addresses of networks
Router sends the IP packet to its destination network
Once the packet reaches its destination network, it is delivered to its final destination host with another mechanism (we discuss later)
Q1: How do we represent the addresses of the networks?
Interface 1
Interface 2
Interface 3
Network Address | Outgoing Interface
METU | Interface 1
CMU | Interface 2
STANFORD | Interface 2
COMPANY 1 | Interface 3

## Slide 23: IP Addresses and Network Addresses
Look at these two IP addresses from METU:
  144.122.144.188 144.122.150.76
IP addresses of all hosts in a network begin with the same block of bits
Host IP addresses are given from a contiguous IP address block
A1: The network address is a number of most significant bits of the IP address
Network
address
Host Address
Network
address
Host Address

## Slide 24: What does a forwarding table look like?
Q2: How does the router represent the network addresses in the routing table?
A2: Routers use a group of most significant bits of 32 bit IP addresses to represent the network addresses in the table.
Network Address | Outgoing Interface
METU | Interface 1
CMU | Interface 2
STANFORD | Interface 2
COMPANY 1 | Interface 3
Address (begins with) | Outgoing Interface
144.122 | Interface 1
128.2 | Interface 2
171.64 | Interface 2
83.66.162 | Interface 3

## Slide 25: How does the router look up an IP packet?
IP packets still carry the individual host addresses
Q3: How does the router find out about the destination network from the IP packet?
Interface 1
Interface 2
Interface 3
144.122.144.88
Network Address | Outgoing Interface
METU | Interface 1
CMU | Interface 2
STANFORD | Interface 2
COMPANY 1 | Interface 3

## Slide 26: IP Addresses and Network Addresses
A3: The router should find how many most significant bits make up the network address for an incoming IP packet.
Then it can extract the network address

## Slide 27: Network Address finding: How many most significant bits
Class-based address: Coarse network addresses
CIDR: Classless Inter Domain Routing: Network address can take any number of bits

## Slide 28: Subnets: Network in CIDR
What’s a subnet ?
  Devices that can physically reach each other without intervening router
How to determine the subnets?
  detach each interface from its host or router,
  creating islands of isolated networks.
  Each isolated network is called a subnet.
Each subnet is assigned a subnet number
Interface 1
Interface 2
Interface 3
223.24.0.0/20
223.24.8.0/22
223.24.16.0/21

## Slide 29: Subnets and addressing
IP address:
  subnet part (high order bits)
  host part (low order bits)
Subnet addresses:
  All interfaces in the subnet have the same subnet part
  Subnet address in human readable form:
223.24.16.0/21
  Binary:
11011111 00011000 00010000 00000000
Host address: 223.24.19.167
11011111 00011000 00010011 10100111
Host address: 223.24.23.15
11011111 00011000 00010111 00001111
Interface 1
Interface 2
Interface 3
223.24.0.0/20
223.24.8.0/22
223.24.16.0/21
223.24.19.167
223.24.23.15

## Slide 30: IP addressing: CIDR
11011111 00011000 00010000 00000000
subnet
part
host
part
First 21 bits of 223.24.16.0
How many hosts can exist in this subnet?
  Subnet part=21 bits
  Hosts part=32-21=11 bits
  211=2K hosts
Notes:   address format: a.b.c.d/x
  x is # bits in subnet portion of address (Higher order bits)
  Less significant 32-x bits are represented as 0

## Slide 31: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  Used in the routers’ forwarding tables
  subnet portion of address of arbitrary length
Logical:
  Subnet address: 11011111 00011000 00010 (21 bits)
  Represented as: 223.24.16.0/21 (for humans)
11011111 00011000 00010000 00000000
subnet
part
host
part
First 21 bits of 223.24.16.0
Q: How can the router represent subnet addresses in the routing table?
Notes:   address format: a.b.c.d/x
  x is # bits in subnet portion of address (Higher order bits)
  Less significant 32-x bits are represented as 0

## Slide 32: IP addressing: CIDR
11011111 00011000 00010000 00000000
subnet
part
host
part
First 21 bits of 223.24.16.0
A: Each network address is stored with a Subnet mask
  Bit pattern to be AND’ed with the 32 bit address
  Indicates which bits are subnet number and which are host number
  Lining up the IP address and the subnet mask together, the network and host portions of the address can be separated
  DETERMINES THE SUBNET ADDRESS FOR AN IP ADDRESS
Address | Mask
11011111 00011000 00010000 00000000 | 11111111 11111111 11111000 00000000
Notes:   address format: a.b.c.d/x
  x is # bits in subnet portion of address (Higher order bits)
  Less significant 32-x bits are represented as 0

## Slide 33: Routing Table IP lookup
Address | Mask | Int
11011111 00011000 00000000 00000000 | 11111111 11111111 11110000 00000000 | 1
11011111 00011000 00001000 00000000 | 11111111 11111111 11111100 00000000 | 2
11011111 00011000 00010000 00000000 | 11111111 11111111 11111000 00000000 | 3
Actual
Subnet | Interface
223.24.0.0/20 | 1
223.24.8.0/22 | 2
223.24.16.0/21 | 3
Logical
Interface 1
Interface 2
Interface 3
Subnet A:
223.24.0.0/20
Subnet B:
223.24.8.0/22
Subnet C:
223.24.16.0/21

## Slide 34: CIDR –Look-up: Example 1
A packet comes in addressed to 223.24.19.167
Binary: 11011111 00011000 00010011 10100111
Packet address is Boolean ANDed with Subnet A mask 11011111 00011000 00010011 10100111
11111111 11111111 11110000 00000000
11011111 00011000 00010000 00000000
A:11011111 00011000 00000000 00000000
Address Mask
A: 11011111 00011000 00000000 00000000 11111111 11111111 11110000 00000000
B: 11011111 00011000 00001000 00000000 11111111 11111111 11111100 00000000
C: 11011111 00011000 00010000 00000000 11111111 11111111 11111000 00000000
NO MATCH!
ROUTER’S FORWARDING TABLE
BOOL AND
Subnet | Interface
223.24.0.0/20 | 1
223.24.8.0/22 | 2
223.24.16.0/21 | 3
Dest Address
Mask of A
AND Result
A address

## Slide 35: CIDR –Look-up: Example 1
A packet comes in addressed to 223.24.19.167
Binary: 11011111 00011000 00010011 10100111
Packet address is Boolean ANDed with Subnet B mask 11011111 00011000 00010011 10100111
11111111 11111111 11111100 00000000
11011111 00011000 00010000 00000000
B:11011111 00011000 00001000 00000000
ROUTER’S FORWARDING TABLE
Address Mask
A: 11011111 00011000 00000000 00000000 11111111 11111111 11110000 00000000
B: 11011111 00011000 00001000 00000000 11111111 11111111 11111100 00000000
C: 11011111 00011000 00010000 00000000 11111111 11111111 11111000 00000000
Subnet | Interface
223.24.0.0/20 | 1
223.24.8.0/22 | 2
223.24.16.0/21 | 3
NO MATCH!
BOOL AND
Dest Address
Mask of B
AND Result
B address

## Slide 36: CIDR –Look-up: Example 1
A packet comes in addressed to 223.24.19.167
Binary: 11011111 00011000 00010011 10100111
Packet address is Boolean ANDed with Subnet C mask
11011111 00011000 00010011 10100111
11111111 11111111 11111000 00000000
11011111 00011000 00010000 00000000
C:11011111 00011000 00010000 00000000
MATCH!
->Forward
to
interface
3
ROUTER’S FORWARDING TABLE
Address Mask
A: 11011111 00011000 00000000 00000000 11111111 11111111 11110000 00000000
B: 11011111 00011000 00001000 00000000 11111111 11111111 11111100 00000000
C: 11011111 00011000 00010000 00000000 11111111 11111111 11111000 00000000
Subnet | Interface
223.24.0.0/20 | 1
223.24.8.0/22 | 2
223.24.16.0/21 | 3
BOOL AND
Dest Address
Mask of C
AND Result
C address

## Slide 37: CIDR –Look-up: Example 2
A packet comes in addressed to 223.24.11.196
Binary: 11011111 00011000 00001011 11000100
Packet address is Boolean ANDed with Subnet A mask
11011111 00011000 00001011 11000100
11111111 11111111 11110000 00000000
11011111 00011000 00000000 00000000
A:11011111 00011000 00000000 00000000
Address Mask
A: 11011111 00011000 00000000 00000000 11111111 11111111 11110000 00000000
B: 11011111 00011000 00001000 00000000 11111111 11111111 11111100 00000000
C: 11011111 00011000 00010000 00000000 11111111 11111111 11111000 00000000
ROUTER’S FORWARDING TABLE
Subnet | Interface
223.24.0.0/20 | 1
223.24.8.0/22 | 2
223.24.16.0/21 | 3
MATCH!
BOOL AND
Dest Address
Mask of A
AND Result
A address

## Slide 38: CIDR –Look-up: Example 2
A packet comes in addressed to 223.24.11.196
Binary: 11011111 00011000 00001011 11000100
Packet address is Boolean ANDed with Subnet B mask
11011111 00011000 00001011 11000100
11111111 11111111 11111100 00000000
11011111 00011000 00001000 00000000
B: 11011111 00011000 00001000 00000000
Address Mask
A: 11011111 00011000 00000000 00000000 11111111 11111111 11110000 00000000
B: 11011111 00011000 00001000 00000000 11111111 11111111 11111100 00000000
C: 11011111 00011000 00010000 00000000 11111111 11111111 11111000 00000000
ROUTER’S FORWARDING TABLE
Subnet | Interface
223.24.0.0/20 | 1
223.24.8.0/22 | 2
223.24.16.0/21 | 3
MATCH!
BOOL AND
Dest Address
Mask of B
AND Result
B address

## Slide 39: CIDR –Look-up: Example 2
A packet comes in addressed to 223.24.11.196
Binary: 11011111 00011000 00001011 11000100
Packet address is Boolean ANDed with Subnet C mask
11011111 00011000 00001011 11000100
11111111 11111111 11111000 00000000
11011111 00011000 00001000 00000000
C: 11011111 00011000 00010000 00000000
Address Mask
A: 11011111 00011000 00000000 00000000 11111111 11111111 11110000 00000000
B: 11011111 00011000 00001000 00000000 11111111 11111111 11111100 00000000
C: 11011111 00011000 00010000 00000000 11111111 11111111 11111000 00000000
ROUTER’S FORWARDING TABLE
Subnet | Interface
223.24.0.0/20 | 1
223.24.8.0/22 | 2
223.24.16.0/21 | 3
NO MATCH!
BOOL AND
Dest Address
Mask of C
AND Result
C address

## Slide 40: Longest Prefix Match (LPM)
If there is more than one match:
Select the match with longer prefix 
  A Smaller subnet with less number of hosts
  Indicates a more detailed match to destination address
For Example 2:
  Match with Subnet A (address of 20 bits, hosts 212) Interface 1
  Match with Subnet B (address of 22 bits, hosts 210) Interface 2
  Select Interface 2

## Slide 41: Summary
Ak: A k bit subnet addresses:
  Represented in 32 bits
  Least significant 32-k bits are zero
Representation of Ak in the forwarding table:
  32 bit subnet address, 32 bit subnet mask
  SM(Ak): Subnet mask for Ak : Most significant k bits are 1, rest are zero

## Slide 42: Summary
IP addresses of all hosts in subnet Ak:
  Start with the same k bits
  Differ in the last 32-k bits
  Maximum number of hosts=232-k
Is a host with address H is in Ak means:
  Are first k bits of H and Ak the same?
  Check: H AND SM(Ak)= Ak
  Remember: The least significant 32-k bits of Ak are 0 already

## Slide 43: Special IP addresses
IP broadcast address:
  255.255.255.255 (limited-reserved)
  A message sent to a broadcast address is typically received by all network-attached hosts, rather than by a specific host.
  Subnet broadcast address:
"this" host on "this" network
  0.0.0.0 (reserved)
11001000 00010111 00010001 11111111
subnet
part
host
part
200.23.17.255

## Slide 44: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: Control Panel\Network and Internet\Network Connections: Adapter Properties, TCP/IPv4
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
  Application layer protocol, runs over UDP

## Slide 45: DHCP: Dynamic Host Configuration Protocol
Allows host to dynamically obtain its IP address from network server when it joins network
  Can renew its lease on address in use
  Allows reuse of addresses (only hold address while connected an “on”)
  Support for mobile users who want to join network (more shortly)
  Application layer protocol runs over UDP

## Slide 46: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
DHCP
server
arriving DHCP
client needs
address in this
network
223.1.2.5

## Slide 47: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
time
DHCP discover (UDP)
src : IP: 0.0.0.0, Port: 68
dest.: IP: 255.255.255.255, Port: 67
Allocated IP address: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
Allocated IP address: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
Allocated IP address: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
Allocated IP address: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
There can be multiple offers if there are multiple DHCP servers
Client accepts an offer and replies
http://support.microsoft.com/kb/169289

## Slide 48: DHCP: more than IP address
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 49: DHCP Example

## Slide 50: IP addresses: how to get one?
Q: How does some network get the subnet part of its IP address block?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 51: Hierarchical addressing: route aggregation
Networks advertise routing information to routers
This information is used to build the routing tables
Hierarchical addressing allows efficient advertisement of routing information:
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 0
Organization 7
Internet
Organization 1
ISP B
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
199.31.0.0/16

## Slide 52: Hierarchical addressing: more specific routes
Organization 1 is moved to ISP B
IP addresses of the hosts in Organization 1 are maintained.
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 0
Organization 7
Internet
Organization 1
ISP B
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
199.31.0.0/16

## Slide 53: Hierarchical addressing: Longest prefix Match (LPM)
11001000 00010111 00010011 10011010 200.23.19.154
11001000 00010111 00010000 00000000 200.23.16.0/20
11001000 00010111 00010010 00000000 200.23.18.0/23
Select Interface 2 with longer prefix match Longer prefix indicates a more detailed match to destination address
Destination is in Organization 1

## Slide 54: IP addressing: the last word...
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 55: IP Address Allocation
1981 - IPv4 protocol published
1985 ~ 1/16 of total space
1990 ~ 1/8 of total space
1995 ~ 1/3 of total space
2000 ~ 1/2 of total space
2002.5 ~ 2/3 of total space
Conserving effort: Network Address Translation
http://www.potaroo.net/tools/ipv4/index.html

## Slide 56: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
Datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
All datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,
different source port numbers
devices inside local net not explicitly addressable, visible by outside world

## Slide 57: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus).

## Slide 58: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 59: NAT Example
Windows cmd: ipconfig -all
https://www.whatismyip.com/
Try with different devices at home 

## Slide 60: No NAT Example 

## Slide 61: NAT: Network Address Translation
Implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr.
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!

## Slide 62: NAT Problems
NAT is controversial:
  routers should only process up to layer 3
NAT breaks “end-to-end communication”
  Routers monitor the communication
  Routers change the data
NAT breaks “Bi-directional communication”
  Hosts with global address can not initiate the communication to the hosts with private address.
Address shortage should instead be solved by IPv6

## Slide 63: IPv6
Initial motivation: 32-bit address space soon to be completely allocated.
Additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
  IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed
  Datagrams larger than MTU are dropped

## Slide 64: IPv4 & IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4 Header
IPv6 Header
- field’s name kept from IPv4 to IPv6
- fields not kept in IPv6
- Name & position changed in IPv6
- New field in IPv6
Legend

## Slide 65: Summary of Header Changes between IPv4 & IPv6
Streamlined
  Fragmentation fields moved out of base header
  IP options moved out of base header
  Header Checksum eliminated
  Header Length field eliminated
  Length field excludes IPv6 header
  Alignment changed from 32 to 64 bits
Revised
  Time to Live ’ Hop Limit
  Protocol ’ Next Header
  Precedence & TOS ’ Traffic Class
  Addresses increased 32 bits ’ 128 bits
Extended
  Flow Label field added

## Slide 66: Summary of Main IPv6 Benefits
Expanded addressing capabilities
Structured hierarchy to manage routing table growth
Streamlined header format and flow identification
Improved support for options / extensions
Security - Built-in, strong IP-layer encryption and authentication
Mobility - More efficient and robust mechanisms
Quality of Service
Notes: Note that Quality of Service is not one of the benefits of IPv6 over IPv4, despite what you may have heard. Both versions of IP have exactly the same QoS features defined. The only difference is the presence of the Flow Label field in IPv6, which allows more efficient packet classification by routers, but this is really a minor implementation optimization, rather than a significant new QoS feature.

## Slide 67: IPv6 History

## Slide 68: IPv6 Reality
Started at 1996
2012 World IPv6 Launch Day
  the goal for World IPv6 Day was to provide only one percent of users with IPv6 access.
  This "is enough traffic to demonstrate that access providers are well advanced in their actual deployment plans.
No one gets the full benefit of IPv6 deployment until everyone supports it.
While IPv6 DNS traffic has tripled over the last year, no significant increase in the percentage of transactions carried over IPv6 for .com and .net
Only deployed because there are no IPv4 address blocks left!

## Slide 69: Transition From IPv4 To IPv6
Not all routers can be upgraded simultaneous
  How will the network operate with mixed IPv4 and IPv6 routers?
Tunneling: IPv6 carried as payload in IPv4 datagram among IPv4 routers

## Slide 70: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
IPv4
IPv4

## Slide 71: Network Layer