## Slide 1: Network Layer Part II: Routing

## Slide 2: Questions
How does the router build the routing table?
How do you control the over all operation of the network layer?
  Getting IP addresses: DHCP
  Routing: OSPF, BGP, RIP
  Network Management: SNMP
  Errors: ICMP

## Slide 3: Interplay between routing, forwarding
Q: How does the router compute the routing table?
Collect information about the network
Use this information as input to a routing algorithm
These are all slow processes (in msec scale)
Can be done in software
Remember:
Address lookup and forwarding is done for every packet
nanosecond scale operation
done in hardware

## Slide 4: Fundamentals for routing table computation: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (u,w), (v,w),
(x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 5: Fundamentals for routing table computation: Graph abstraction costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(p,q) = cost of link (p,q)
- e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
Cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
Question: What’s the least-cost path between u and z ?
Routing algorithm: algorithm that finds least-cost path

## Slide 6: Routing
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
A/M: Address/Subnet Mask pair
Task of u:
Find the least cost path to all routers (all subnets)
Determine Outgoing interface of u on the least cost path to all subnets
ALL ROUTERS DO THE SAME SUCH THAT ALL PACKETS FOLLOW THE LEAST COST PATHS TO THEIR DESTINATIONS

## Slide 7: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 8: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s

## Slide 9: Dijsktra’s Algorithm (for node u)
1 Initialization:
2 N' = {u}
3 for all nodes r
4 if r adjacent to u
5 then D(r) = c(u,r)
6 else D(r) = ∞
7
8 Loop
9 find q not in N' such that D(q) is a minimum
10 add q to N'
11 update D(r) for all r adjacent to q and not in N' :
12 D(r) = min( D(r), D(q) + c(q,r) )
13 /* new cost to r is either old cost to r or known
14 shortest path cost to q plus cost from q to r */
15 until all nodes in N'
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(r): current value of cost of path from source to dest. r
p(r): predecessor node along path from source to r
N': set of nodes whose least cost path definitively known

## Slide 10: Dijkstra’s algorithm: example
Step
0
N'
u
D(v),p(v)
2,u
D(w),p(w)
5,u
D(x),p(x)
1,u
D(y),p(y)
∞
D(z),p(z)
∞
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Initialization:
N' = {u}
for all nodes r
if r adjacent to u
then D(r) = c(u,r)
else D(r) = ∞
Notation:
N': set of nodes whose least cost path definitively known
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(r): current value of cost of path from source to dest. r
p(r): predecessor node along path from source to r

## Slide 11: Dijkstra’s algorithm: example
Step
0
1
N'
u
u, x
D(v),p(v)
2,u
2,u
D(w),p(w)
5,u
4,x
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
find q not in N' such that D(q) is a minimum
add q to N'
update D(r) for all r adjacent to q and not in N' :
D(r) = min( D(r), D(q) + c(q,r) )
until all nodes in N'

## Slide 12: Dijkstra’s algorithm: example
Step
0
1
2
N'
u
u, x
u, x, y
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
find q not in N' such that D(q) is a minimum
add q to N'
update D(r) for all r adjacent to q and not in N' :
D(r) = min( D(r), D(q) + c(q,r) )
until all nodes in N'

## Slide 13: Dijkstra’s algorithm: example
Step
0
1
2
3
N'
u
u, x
u, x, y
u, x, y, v
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
find q not in N' such that D(q) is a minimum
add q to N'
update D(r) for all r adjacent to q and not in N' :
D(r) = min( D(r), D(q) + c(q,r) )
until all nodes in N'

## Slide 14: Dijkstra’s algorithm: example
Step
0
1
2
3
4
N'
u
u, x
u, x, y
u, x, y, v
u, x, y, v, w
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
find q not in N' such that D(q) is a minimum
add q to N'
update D(r) for all r adjacent to q and not in N' :
D(r) = min( D(r), D(q) + c(q,r) )
until all nodes in N'

## Slide 15: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
u, x
u, x, y
u, x, y, v
u, x, y, v, w
u, x, y, v, w, z
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
find q not in N' such that D(q) is a minimum
add q to N'
update D(r) for all r adjacent to q and not in N' :
D(r) = min( D(r), D(q) + c(q,r) )
until all nodes in N'

## Slide 16: Dijkstra’s algorithm: example
Resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
Resulting forwarding table in u:
2
1
2
3
4
total cost
u
y
x
w
v
z
2
1
1
1
2
A1/M1
A2/M2
A3/M3
A4/M4
A5/M5
(u,v)
(u,v)
(u,x)
(u,y)
(u,w)
destination
Link (interface)
Resulting forwarding table in u:
A6/M6
(u,z)
A6/M7
(u,z)

## Slide 17: Dijkstra’s algorithm, discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, q, not in N’
n(n-1)/2 comparisons: O(n2)
more efficient implementations possible: O(nlogn)
Oscillations possible:
e.g., link cost = amount of carried traffic
Prefer low cost links increase the amount of traffic increase the link cost  now low cost links are different route has to be recomputed

## Slide 18: A Distance Vector Algorithm
Bellman-Ford’s algorithm
Each node receives information only from its directly connected neighbors
Iterative: Stops when there is no more information to exchange
The nodes do not have to compute at the same time (asynchronous)

## Slide 19: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time varies
Speed of Convergence
LS: O(n2) algorithm requires O(nE) msgs
  may have oscillations
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagates through the network

## Slide 20: Hierarchical Routing
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network

## Slide 21: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
An AS is a connected group of one or more IP prefixes run by one or more network operators which has a SINGLE and CLEARLY DEFINED routing policy.
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
Border Gateway router
Direct link to router in another AS

## Slide 22: Internet AS Hierarchy

## Slide 23: Example

## Slide 24: Intra-AS Routing
Also known as Interior Gateway Protocols (IGP)
Most common Intra-AS routing protocols:
  RIP: Routing Information Protocol: Distance Vector
  OSPF: Open Shortest Path First: Link State
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)
  IS-IS: Intermediate System to Intermediate System: Link State

## Slide 25: OSPF (Open Shortest Path First)
“open”: publicly available
uses Link State algorithm
  LS packet dissemination
  topology map at each node
  route computation using Dijkstra’s algorithm
advertisements disseminated to entire AS (via flooding)
  carried in OSPF messages directly over IP (rather than TCP or UDP

## Slide 26: OSPF “advanced” features (not in RIP)
security: all OSPF messages authenticated (to prevent malicious intrusion)
multiple same-cost paths allowed (only one path in RIP)
For each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort; high for real time)
hierarchical OSPF in large domains.

## Slide 27
summarize” distances to nets in own area, advertise to other Area Border routers.
run OSPF routing
limited to backbone.
connect to other AS’s
  Link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
local area
backbone
two-level hierarchy
Hierarchical OSPF

## Slide 28: Internet AS Hierarchy

## Slide 29: Inter-AS tasks
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
How does router 1d in AS1 install routing table entry for some far away subnet x:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which destinations are reachable through AS2 and AS3
propagate this reachability info to all routers in AS1
Job of inter-AS routing!
x

## Slide 30: Example: Setting forwarding table in router 1d
suppose AS1 learns (via inter-AS protocol) that subnet x is reachable via AS3 (gateway 1c) but not via AS2.
inter-AS protocol propagates reachability info to all internal routers in AS1:
For all AS1 routers: if you want to forward a packet to subnet x send it to router 1c
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
x
…
K

## Slide 31: Example: Setting forwarding table in router 1d
For all AS1 routers: if you want to forward a packet to subnet x send it to router 1c
router 1d determines from intra-AS routing info that its interface K is on the least cost path to 1c.
  installs forwarding table entry (x,K)
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
x
…
K

## Slide 32: Example: Choosing among multiple ASes
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine towards which gateway it should forward packets for dest x.
  install forwarding table entry (x,K) or (x,P) in 1d?
  this is also job of inter-AS routing protocol!
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
x
…
…
K
P

## Slide 33: Example: Choosing among multiple ASes
Hot potato routing:
  send packet towards the closest of two border routers.
  hands off traffic to a downstream ISP as quickly as it can.
  the goal is to get rid of traffic as soon as possible so as to minimize the amount of work that the ISP's network needs to do.
Cold-potato routing:
  ISP carries traffic as far as possible on its own network before handing it off to a downstream ISP.
  the goal is carry traffic on the ISP's network as long as possible to maximize the control that the ISP has on the end-to-end quality of service.
In general, an ISP's routing policy would lie somewhere in between the extremes of hot-potato and cold-potato routing.

## Slide 34: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto standard
BGP provides each AS a means to:
  Obtain subnet reachability information from neighboring ASs.
  Propagate reachability information to all AS-internal routers.
  Determine “good” routes to subnets based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 35: Remember: Hierarchical addressing
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 0
Organization 7
Internet
Organization 1
ISP B
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
199.31.0.0/16
BGP advertisements

## Slide 36: BGP basics
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
e(xternal) BGP session
i(nternal) BGP session
BGP sessions: pairs of routers (BGP peers) exchange routing info over semi-permanent TCP connections
need not correspond to physical links.

## Slide 37: BGP sessions
external BGP (EBGP)
  exchanges between different ASs
  to perform inter-AS routing.
internal BGP (IBGP)
  exchanges within a single AS.
  to perform intra-AS routing.
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
e(xternal) BGP session
i(nternal) BGP session

## Slide 38: Distributing reachability info
using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
  1c can then use iBGP do distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
when router learns of new prefix, it creates entry for prefix in its forwarding table.
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
eBGP session
iBGP session

## Slide 39: Distributing reachability info
when AS2 advertises a prefix to AS1:
  AS2 promises it will forward datagrams towards that prefix.
  AS2 can aggregate prefixes in its advertisement
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
e(xternal) BGP session
i(nternal) BGP session

## Slide 40: Remember: Routing Advertisements
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 0
Organization 7
Internet
Organization 1
ISP B
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
199.31.0.0/16
Aggregated BGP advertisement

## Slide 41: BGP routing policy Example
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
  X does not want to route from B to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 42: BGP routing policy (2)
A advertises path AW to B
B advertises path BAW to X
B does not advertise path BAW to C
  B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to W via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 43: Why different Intra- and Inter-AS routing ?
Policy:
Inter-AS: admin wants control over how its traffic routed, who routes through its net.
Intra-AS: single admin, so no policy decisions needed
Scale:
hierarchical routing saves table size, reduced update traffic
Performance:
Intra-AS: can focus on performance
Inter-AS: policy may dominate over performance

## Slide 44: The largest AS: Level 3
http://icaruswept.com/2016/06/28/who-owns-the-internet/
AS’s customer cone: the set of ASes an AS can reach using customer links.
Level 3 Customer Cone: 30,814

## Slide 45: Network Layer Part II: Routing